## Slide 1: Project Management

## Slide 2: There are Three Stages to a Project
Pre – Construction Stage
Construction Stage
Post Construction Stage

## Slide 3: Pre - Construction
Concept and Proposals
Feasibility
Cost Plan
Design
Cost
Health and Safety Plan/File
Risk Management
Site Investigation
Tender Process

## Slide 4: Pre – Construction Team
Client. Two types of client?
Project Manager
Architect
Quantity Surveyor
Contracts Manager
Buyer
Specialist Engineers
Specialist Designers
Clerk of Works

## Slide 5: Construction Stage
Establish boundaries
Site set up
Site Clearance
Sub – structure and Services
Super – structure
Finishes
Landscape
Handover
Defects Liability Period
Final Account

## Slide 6: Construction Team
Contractor
Site Manager
Quantity Surveyor
Health and Safety Inspector
Site Clerk
General Foreman
Craft Foreman
Trades Persons
Operatives
Sub - Contractors

## Slide 7: The Contractor
The contractor is the person or organisation who will actually undertake the work to complete the project. He will employ direct or indirect labour to complete the work. Direct labour are personnel who would be employed directly by the contractor. Indirect labour would be people classed as sub – contractors to carry out specialist work on the project such as landscaping etc.

## Slide 8: Site Manager
The site manager will have overall control of what occurs on the construction site. All operations and activities that take place on the site will be sanctioned by him. He will have responsibility for Health, Safety and Welfare facilities, the timescale of the work and general organisation of the resources to carry out the work effectively.

## Slide 9: Contractor’s Quantity Surveyor
Responsible for making sure the project is carried out within budget. He will also work closely with the contracts manager and site manager to report and record any extra work that arises from variations and instructions from the architect. He will be responsible for calculating monthly interim payment sums and will attend site meetings with the client’s Principal Quantity Surveyor (QS) to determine the value of the work to be included in the payment that is due for that working month.

## Slide 10: Health and Safety Officer
Ultimately responsible for all Health, Safety
and Welfare issues regarding the workplace.
Also responsible for inquiries should accidents
or near misses occur in the workplace. Should
always be proactive in their approach to
workplace safety. Should vigilantly monitor risk
Assessments and method statements.

## Slide 11: Craftsperson
Bricklayer
Carpenter
Plasterer
Painter and decorator
Wall tiler
Roofer
Dry liner

## Slide 12: Craftsperson
These are the specialist operatives that will carry out the work on the project. For example, a bricklayer will actually erect the building and build any boundary walls required. A carpenter will carry out all wood related work including constructing the roof, laying first floor floors and finishing off all second fix carpentry including architraves, skirting boards and hanging internal and external doors.

## Slide 13: Sub – Contract Labour
Any type of labour used on site that is not directly employed by the contractor. For example, nominated electrical company previously used by the client. Sub – contract bricklayers taken on for a specific job where there is a large amount of brickwork not suitable for the company’s direct workforce or where the work has fallen behind.

## Slide 14: Post Construction
On completion of the project, the site ownership reverts back to the client. When all contractual obligations are met on handover then the defects liability period begins. When this has run it’s course then final payment is made. However, there now begins a period where the building has to be managed. This will be the responsibility of the estates department and the facilities team.

## Slide 15: Post Construction
They will be responsible for:
Building maintenance
Landscaping
Repairs
Refurbishment/alterations
Housekeeping
Staffing

## Slide 16: Construction Management
Construction management is a term used when an organisation undertakes a project in a management capacity only. They will not actually construct the project, rather, manage the resources in particular the labour resources by sub – contracting out the work and managing the site and its activities.

## Slide 17: The Construction Triangle