## Slide 1: Mechanical Seal Replacement
Case Study:
4” centrifugal effluent pump

## Slide 2: SAFETY FIRST
Local isolation or remote isolation.
Different drive sources for the pump can vary but all can be isolated.

## Slide 3: PPE (PERSONAL PROTECTIVE EQUIPMENT)
Gloves
Goggles
Safety boots
Hi-Vis Situation dependant
Ear defenders ie; ships engine room
Hard hat
Cloths peg

## Slide 4: CLEANING, FLUSHING THE PUMP
Contamination risk from fluids.
Diesel (Dermatitis).
Chemical (Corrosive)
Effluent (Biological)

## Slide 5: DISASSEMBLY
Once open, not all pumps look the same. Different purpose, different type.
Here a stator plate is fitted for maceration effect.

## Slide 6: STATOR REMOVAL
Once the stator plate is removed the basic function is the same

## Slide 7: ROTOR REMOVAL
Locking the shaft.
Right or left-handed thread?
Parallel or tapered shaft?
Workshop manual

## Slide 8: SHIMS
Pretention on the seal faces.
Measure.
Refer to manual
Notes: Be careful to remove and store the shims as they are critical to the reassembly.

## Slide 9: NEW PARTS
Check the new seal for damage.
Measure spring length before fitting.

## Slide 10: THE SEAL
Different face materials depending on manufacturer.
Removal requires access to the back of the pump body.
When replacing, the seal should be set on sealant or grease to form a watertight seal.
Take care not to damage the face of the seal.

## Slide 11: THE SEAL FACE
Care must be taken with the face of the seal as it is very brittle.
Woodruff key to be removed and checked for wear.
When replacing care must be taken to keep square.
This part of the seal should also be fitted with sealant or grease.

## Slide 12: REFITTING THE ROTOR
When refitting the rotor a seal must be made on the bolt.

## Slide 13: REASSEMBLY
Check the valves.
Clean the body seal faces.
Check the body seal

## Slide 14: LEAK TESTING
Fill the pump.
Bleed the air
Static test
Run the pump
Final commissioning

## Slide 15: CONCLUSION
Were possible read the manual first
Always check the new parts before commencement
Keep safe
Keep others safe
Work clean

## Slide 16: JOB WELL DONE