L3 Land-based Service Engineering - Task Sheet

NAME:.....................................................................................	DATE:................

Reference:	Task:

306/09	MEASURING PISTON RING GAPS

Requirements:

Dismantled or short engine

Feeler gauge

Engine manual/data.

Instructions:

Dismantle engine as required to gain access

Insert piston ring into bore as appropriate and measure gap.

(An Activity Sheet will not be required for this task)

Method:

1.	Prepare engine by part dismantling until piston assemblies are removed.  Ensure block face of engine is uppermost and secure.

2.	Insert piston ring/s into selected bore and using a previously removed piston head upside down, push ring squarely down the bore until just below the top of the bore.

3.	Measure the ring gap with a feeler gauge and record your findings on the proforma over.

4.	Now push the ring further down below the top of the ‘swept’ area (unless engine had been re-bored) and measure the ring gap again and record your findings.

GET SUPERVISOR FOR INSPECTION AT THIS POINT

over/

QUESTIONS

1.	What would be an acceptable ring gap for a water-cooled engine?

(thou per inch of bore)

2.	What would be an acceptable ring gap for an air-cooled engine?

(thou per inch of bore)

3.	Now convert these measurements into metric SI units.

(SI = Système International: the international system of metric units)

4.	State what would likely happen if ring gaps were outside these tolerances both plus and minus.

| RING GAP | TOP OF BORE | BELOW TOP |
| --- | --- | --- |
| CYL |  |  |

TASK COMPLETE

Signed (Trainee):..........................................................	Date:...............................

Signed (Assessor):.......................................................	Date:...............................