L3 Land-based Service Engineering - Task Sheet

NAME:.....................................................................................	DATE:................

Reference:	Task:

306/11	CHECKING ENGINE LUBRICATION PUMP FOR WEAR

Requirements:

Rule

Feeler gauge

Engine manual.

Instructions:

Check engine lubrication pump for serviceability.

Method:

1.	Remove engine lubrication pump as required.

2.	Dismantle pump as required and thoroughly clean all components.

Check for scoring/damage on internal components and re-assemble loosely.

3.	Measure end clearance of rotor in body using feeler gauge and rule.  Note measurement over.

4.	Measure clearance between outer rotor and pump body.  Note measurement over.

5.	Measure clearance between pump lobe and rotor lobe at 12 o’ clock (out of mesh).  Note measurement over.

over/

| MEASUREMENTS mm / thou | MEASURED | MINIMUM CLEARANCE |
| --- | --- | --- |
| ROTOR TO ENDPLATE |  | 0.635mm 0.0025” |
| ROTOR TO BODY |  | 0.02mm 0.008” |
| PUMP LOBE TO ROTOR LOBE |  | 0.152mm 0.006” |

QUESTIONS

1.	What engine was the pump removed from?

2.	Describe the condition of this pump and whether this is still serviceable or a scrapper?

3.	What are the symptoms of low engine oil pressure and likely consequences?

4.	What are the main reasons for a pump to wear out prematurely?

TASK COMPLETE

Signed (Trainee):..........................................................	Date:...............................

Signed (Assessor):.......................................................	Date:...............................