L3 Land-based Service Engineering - Task Sheet

NAME:.....................................................................................	DATE:................

Reference:	Task:

309/01	PERFORM A FLOWMETER TEST

Requirements:

Machine with relevant take-off points

Flowmeter

Appropriate hydraulic couplings & adapters

Hydraulic data for machine.

Instructions:

Obtain relevant data for hydraulic pressures & flows

Measure pressure & flow hydraulic circuit

Test Pressure Relief Valve (where appropriate)

Record results & compare against manufacturer's specifications.

Method:

1.	Break into the circuit to be tested & attach Flowmeter.

2.	Ensure load valve fully open and start engine and run at recommended speed.

3.	With total flow passing through the Flowmeter, slowly close the load valve and take readings at appropriate steps.  Record your readings on the proforma over.

4.	On completion, open the load valve and commence to test the relief valve where installed in line to circuit.

MANUFACTURERS SPECIFICATION

Machine Make & Model:			Flow rate @ Recommended Speed:		  gpm

Engine Rated Speed:		  rpm	Hydraulic System Pressure:			psi

| PUMP TEST |
| --- |
| Pressure (psi) | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 |
| Output (gpm) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

PRESSURE RELIEF VALVE TEST

Cracking pressure:		  psi	Maximum pressure:		  psi

DETERMINING PUMP EFFICIENCY

Measured pump output at min. pressure = 		  (B)	% Efficiency = A  B x 100

A  B =

Pump output @ 200 psi below system pressure =		  (A) 	x 100% =

tick

Pump condition: > 75% = serviceable	PUMP:	- SERVICEABLE	(

< 75% = recondition	- RECONDITION	(