L3 Land-based Service Engineering - Task Sheet

NAME:.....................................................................................	DATE:................

Reference:	Task:

315/01	TEST BATTERY CONDITION

Requirements:

Suspect battery

Battery Hydrometer

Discharge (drop) tester

Battery charger as necessary

Voltmeter

PPE.

Instructions:

Remove battery & test.

Hand in the proforma sheet (P1) when complete.

Method:

1.	Remove battery from vehicle as required and clean up as necessary.

2.	Measure 'open-circuit' voltage and record readings on P1.

3.	Where applicable remove caps & check/top-up electrolyte level in each 		cell.

4.	Test the state of charge of each cell by using the hydrometer & note 		the readings in the table on P1.

5.	If requiring a charge, connect battery to trickle-charger observing all 		precautions and charge up before continuing with test.

6.	When "gassing" has commenced and charger ammeter shows a 			charge rate of < 1A, switch off & disconnect charger.  Retake SG 			readings to confirm battery charged up.

7.	After gassing has subsided and taking all precautions, hold the 		prods of the 'drop tester' for no longer than 15 seconds to perform a 	discharge test whilst observing the cells.  Record the results on P1.

8.	Measure final 'open-circuit' voltage & record readings on P1.

over/

9.	Check the soundness of the battery terminals & smear them with			petroleum jelly before replacing battery on vehicle if required.

10.	Complete your Inspection Report and attach to this Task Sheet.

QUESTIONS

1.	When disconnecting a battery, why should you remove the earth 			terminal first whether positive or negative earth?

2.	Where should the electrolyte level be:

- above the plates?

- below the plates?

- just below the caps?

3.	What's the name of the acid in batteries?

4.	What happens to this acid as the battery becomes "flat"?

5.	What should be the S.G. of a fully charged cell?

6.	When might this differ slightly but still be OK?

7.	Explain what is meant by “gassing” and state why this may be 			dangerous?

8.	What voltage should you get using the drop tester on a good HD battery and what does it mean if it drops off quickly?

9.	What causes battery post corrosion & how can it be prevented?

10.	Why is it important to keep the top of the battery dry?

HAND IN WITH YOUR PROFORMA

TASK COMPLETE

Signed (Trainee):..........................................................	Date:...............................

Signed (Assessor):.......................................................	Date:...............................