L3 Land-based Service Engineering - Task Sheet

NAME:.....................................................................................	DATE:................

Reference:	Task:

315/04	INSPECT & TEST A COOLING SYSTEM

Requirements:

Water-cooled engine

Inspection lamp

Thermostat tester

Pressure tester

Engine manual/data.

Instructions:

Visually examine the cooling system & check the tick boxes over.

Method:

1.	Examine the radiator & around the header tank for any signs of 			leakage.

2.	Examine the water pump for signs of leakage.  Grasp the fan blades 		carefully & test for any play in the spindle bearings.

3.	Check all hoses by gently squeezing them to see if they have become 		hardened.  Also check for cracking & deterioration.

4.	Inspect around the head gasket for any signs of leakage.

5.	Locate heater valves (if fitted) and check for signs of leakage.  Check 		to see if they are free to turn off.

6.	Remove thermostat and test for serviceability.  Replace or renew.

7.	Pressure test system including pressure cap to confirm serviceability.

8.	Evaluate condition by filling out attached proforma.

over/

QUESTIONS

1.	What could be the effects of a faulty thermostat?

2.	What would be the effect of a failed pressure cap?

3.	Summarize your findings from the proforma on an Inspection Report.

TASK COMPLETE

Signed (Trainee):..........................................................	Date:...............................

Signed (Assessor):.......................................................	Date:...............................