L3 Land-based Service Engineering - Task Sheet

NAME:.....................................................................................	DATE:................

Reference:	Task:

315/08	DISMANTLE AND INSPECT WET DISC BRAKES

Requirements:

Appropriate machine with hydraulic wet disc brakes

Parts cleaner

Trolley jack

Matching axle stands

Appropriate cradle for trumpet housing

Props

Wheel transporter

Drain buckets

Workshop manual.

Instructions:

Dismantle and inspect service brakes on a machine.

Test out on completion

Complete inspection report.

Method:

1.	Thoroughly wash off around trumpet housing & transmission to be worked on.

2.	Drain transmission fluid as appropriate.

3.	Jack up respective side of machine & remove wheel.

4.	Disconnect any attached linkages, hoses and unclip wiring etc.

5.	Disconnect cab mount and prop up.

6.	Prepare cradle & trolley jack and support trumpet housing.

GET SUPERVISOR FOR INSPECTION AT THIS POINT

7.	Remove ring bolts and withdraw trumpet housing.

8.	Dismantle brake components and clean off.

9.	Undertake thorough inspection.

over/

10.	Rebuild brake assembly then replace trumpet housing.

11.	Reinstate machine and refill transmission oil.

12.	Test out on completion then fill out Inspection Report proforma.

QUESTIONS

1.	What was the purpose of the inspection and test:	(tick)

- to check manufacturer’s compliance?	(

- incident occurrence?	(

- for diagnosis?	(

2.	What may you see when you drain the transmission fluid that would 		indicate a problem and what might this problem be?

3.	What would be the consequences if brake friction plates were to wear out completely?

4.	Attach the Inspection Report to this Task Sheet.

TASK COMPLETE

Signed (Trainee):..........................................................	Date:...............................

Signed (Assessor):.......................................................	Date:...............................