# Activity C14: Rate of a Chemical Reaction 1
(Colorimeter)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Rate of reactions | C14 Reaction Rate 1.DS | C14 Reaction Rate 1 | C14_REA1.SWS |

| Equipment Needed | Qty | Chemicals and Consumables | Qty |
| --- | --- | --- | --- |
| Colorimeter (CI-6747) | 1 | Hydrochloric acid, 6 molar | 10 mL |
| Cuvette (w/sensor) | 1 | Sodium thiosulfate, 0.2 molar | 10 mL |
| Graduated cylinder, 10 mL | 2 | Water, distilled | 100 mL |
| Protective gear | PS |  |

## What Do You Think?

How will changing the concentrations of the reactants in a chemical reaction affect the rate of the reaction?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

All chemical reactions occur at specific rates. The rate of a chemical reaction depends on several physical and chemical factors. These factors include:

| • The concentration of the reactants | • The pressure on the reaction |
| --- | --- |
| • The temperature of the reaction | • The presence of a catalyst |

In this activity you will determine the effect of changes in concentration of the reactants on the rate of the chemical reaction. The reaction for this activity is the acidic reduction of the thiosulfate ion to sulfur and sulfur dioxide.

The equation for the reaction is:

S2O32-(aq)   +   2 H+(aq)  =========>  SO2(g)   +   S (s)    +   H2O

One way to determine the effect of concentration on the rate of the reaction is to use a Colorimeter to measure the formation of the solid sulfur generated. The solid sulfur will block the light in the Colorimeter and the amount of blockage is directly proportional to the amount of sulfur in suspension.

The rate of this chemical reaction is given by the equation:

Rate = k [thiosulfate]a [acid]b

The letters a and b seen as exponents are numerals which can only be determined experimentally. Each reactant must be varied separately while the other is kept constant. The effect on the rate of the reaction is noted and the value of the exponent is determined in this way:

•	If a change in concentration of one of the reactants has no effect, the exponent is 0.

•	If doubling the concentration doubles the rate, the exponent is 1.

•	If doubling the concentration quadruples the rate, the exponent is 2.

The over all order of the reaction is determined by adding a + b.

| SAFETY REMINDERS Wear protective gear. Follow directions for using the equipment. Handle and dispose of all chemicals and solutions properly. |  |  |  |
| --- | --- | --- | --- |

## For You To Do

Use the Colorimeter to measure the change in absorbance of light by a solution of sodium thiosulfate and hydrochloric acid as the two components react. Begin with a mixture with specific concentrations of the two components, and then test mixtures with different concentrations of one component or the other. Use DataStudio or ScienceWorkshop to record and display the data. Use the data to determine the overall order of the rate of reaction.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

•	The sensor’s connector cable has a mini-DIN plug at one end and a regular DIN plug at the other.

2.	Plug the mini-DIN end of the cable into the sensor and then connect the other end of the cable into Analog Channel A on the interface.

•	The Colorimeter will automatically turn itself on when it is connected to the ScienceWorkshop interface.

3.	Open the file titled as shown;

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| C14 Reaction Rate 1.DS | C14 Reaction Rate 1 | C14_REA1.SWS |

•	The DataStudio file has a Graph display. Read the Workbook display for more information.

•	The ScienceWorkshop document has a Graph display with absorbance of light versus time.

•	Data recording is set at ten measurements per second (10 Hz).

## PART II: Sensor Calibration and Equipment Setup

### About the Colorimeter

The Colorimeter analyzes colors of light that pass through a solution. The solution is put into a rectangular container called a cuvette, which is then placed inside the Colorimeter. The measure of the amount of light that passes through a solution is called “transmittance”. Transmittance is a ratio of the intensity of the transmitted light to the intensity of the original light, and is usually expressed as a percentage.

Absorbance is related to transmittance. The light absorbed by a solution depends on the absorbing ability of the solution, the distance traveled by the light through the solution, and the concentration of the solution. The relationship of absorbance to transmittance is:

### Calibration

The general method for calibrating the Colorimeter is as follows:

•	First, calibrate the Colorimeter with a clear cuvette containing distilled water.

•	Second, calibrate the software (either DataStudio or ScienceWorkshop) for one of the four colors of light that can be selected in the Colorimeter. (For this activity you will use the RED wavelength.)

Note: The cuvette has two clear sides and two ridged sides.

•	All cuvettes should be wiped clean and dry on the outside with a tissue.

•	Handle cuvettes only by the top edge of the ridged sides.

•	All solutions should be free of bubbles.

•	Always position the cuvette so the light beam will pass through the clear sides.

### Calibrate the Colorimeter

When the Colorimeter comes on, the liquid crystal display (LCD) should say “Please calibrate”.

To calibrate the Colorimeter with a clear cuvette, fill a clean cuvette with distilled water and cap the cuvette. (The clear cuvette is a control or ‘reference’ that accounts for the small amount of light scattered or reflected by the walls of the cuvette.)

On the Colorimeter, press the ‘Select’ button () and the ‘Start/Stop’ button () at the same time.

The Colorimeter’s LCD will say “Insert reference then push SELECT”.

Place the closed cuvette inside the Colorimeter. Make sure that the clear sides of the cuvette (without ridges) are lined up with the light path in the Colorimeter. Close the lid on the Colorimeter.

On the Colorimeter, press the ‘Select’ button.

The Colorimeter will automatically calibrate itself for all four wavelengths assuming that the light passing through the clear cuvette represents “100% Transmittance”. (The automatic calibration takes only a few seconds.)

The Colorimeter’s LCD will say “CAL done, push SELECT or START”.

### Calibrate the Software

Follow these steps to calibrate the software for one of the four colors of light:

1.	Leave the cuvette with distilled water inside the Colorimeter.

2.	In the Experiment Setup window, double-click the Colorimeter icon.

•	In DataStudio, the Sensor Properties window will open. Click the ‘Calibration’ tab. In ScienceWorkshop, the Sensor Setup window will open.

3.	Select the color of light.

•	NOTE: The default color is RED, so you do not need to change the selection for this activity.

4.	Calibrate the software.

•	First, press the ‘Start/Stop’ button () to start the Colorimeter. (The LCD shows the color and wavelength, the percent transmittance, and “RUN”.)

•	Second, check the voltage under ‘Current Reading’ in DataStudio or next to ‘Cur Value:’ in ScienceWorkshop.

•	Third, when the voltage stabilizes, click the ‘Take Reading’ button under ‘High Point’ in DataStudio or the ‘Read’ button in the row for ‘High Value:’ in ScienceWorkshop.

•	Fourth, press the ‘Start/Stop’ button to stop the Colorimeter. (The LCD changes to “STOP”.)

5.	Click ‘OK’ to return to the Experiment Setup window.

•	The software is now calibrated for the Colorimeter.

### Equipment Setup

When sodium thiosulfate and hydrochloric acid are mixed, the solution gradually becomes darker. The solution absorbs more and more light (its absorbance increases).

You will test four solutions made up of different amounts of two reactants as follows:

| Solution | Component A | Component B |
| --- | --- | --- |
| #1 | 1.6 mL of 0.2 M sodium thiosulfate | 1.6 mL of 6 M hydrochloric acid |
| #2 | 1.6 mL of 0.2 M sodium thiosulfate | 0.8 mL of 6 M hydrochloric acid and 0.8 mL of distilled water |
| #3 | 0.8 mL of 0.2 M sodium thiosulfate and 0.8 mL of distilled water | 1.6 mL of 6 M hydrochloric acid |
| #4 | 0.4 mL of 0.2 M sodium thiosulfate and 1.2 mL of distilled water | 1.6 mL of 6 M hydrochloric acid |

The general procedure is as follows:

1.	Measure the liquids needed for Component A into one graduated cylinder.

2.	Measure the liquids needed for Component B into a second graduated cylinder.

3.	Put Component B into a cuvette.

4.	Add Component A to the same cuvette and put a cap on the cuvette.

5.	Quickly invert the cuvette to mix the components.

6.	Quickly put the cuvette into the Colorimeter.

7.	Start the Colorimeter. Record data. Stop the Colorimeter

## PART III: Data Recording

1.	When you are ready to begin data recording, place Component B for the first solution in the cuvette. Add Component A for the first solution to the cuvette. Cap the cuvette, invert it to mix the components, and quickly put the cuvette into the Colorimeter. Close the Colorimeter lid.

2.	Press the ‘Start/Stop’ button () to start the Colorimeter.

3.	Start recording data. (Hint: Click ‘Start’ in DataStudio or click ‘REC’ in ScienceWorkshop.)

4.	Record data for 3 minutes and then stop the data recording.

5.	Press the ‘Start/Stop’ button () to stop the Colorimeter.

6.	Remove the cuvette from the Colorimeter and dispose of the solution as instructed.

7.	Repeat the procedure for solutions 2, 3, and 4. There will be four runs of data at the end of the data recording.

## Analyzing the Data in DataStudio

Use the analysis tools in the Graph display to determine the rate of reaction for each solution. A procedure for doing this is as follows:

1.	Select the run to analyze.

2.	Use the cursor to select a region near the beginning the plot where the absorbance is changing.

3.	Select ‘Linear’ from the ‘Fit’ menu.

4.	Record the value of the slope (‘m’) as the rate of the reaction.

Repeat the process for each run of data.

## Analyzing the Data in ScienceWorkshop

Use the analysis tools in the Graph display to determine the rate of reaction for each solution. A procedure for doing this is as follows:

1.	Select the run to analyze.

2.	Click the ‘Statistics’ button () to open the statistics area. Rescale the display to fit the data.

3.	Use the cursor to select a region near the beginning the plot where the absorbance is changing.

4.	Click the ‘Statistics menu’ button () and select ‘Curve Fit, Linear Fit’ from the menu.

5.	Record the value of a2 as the rate of reaction.

Repeat the process for each run of data.

## Record your results in the Lab Report section.

# Lab Report - Activity C14: Rate of a Chemical Reaction 1

## What Do You Think?

How will changing the concentrations of the reactants affect the rate of a chemical reaction?

## Data Table

| Solution | Rate |
| --- | --- |
| #1 (1.6 mL thiosulfate, 1.6 mL HCl) |  |
| #2 (1.6 mL thiosulfate, 0.8 mL HCl + 0.8 mL water) |  |
| #3 (0.8 mL thiosulfate + 0.8 mL water, 1.6 mL HCl) |  |
| #4 (0.4 mL thiosulfate + 1.2 mL water, 1.6 mL HCl) |  |

## Questions

1.	What is the effect on the rate of the reaction by halving the concentration of thiosulfate?

2.	What is the order of the reaction due to thiosulfate?

3.	What was the effect on the rate of reaction by halving the concentration of acid?

4.	What is the order of the reaction due to acid?

5.	What is the over all order of the reaction?

# Text boxes

Clear sides aligned with light path.