# Activity C15: Rate of a Chemical Reaction 2
(Colorimeter)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Rate of reactions | C15 Reaction Rate 2.DS | C15 Reaction Rate 1 | C15_REA2.SWS |

| Equipment Needed | Qty | Chemicals and Consumables | Qty |
| --- | --- | --- | --- |
| Colorimeter (CI-6747) | 1 | 2-butanol, 2 molar | 10 mL |
| Cuvette (w/sensor) | 1 | Potassium permanganate, 0.2 molar | 10 mL |
| Pipette, 1 mL | 4 | Sulfuric acid, 1 molar | 10 mL |
| Protective gear | PS | Water, distilled | 10 mL |

## What Do You Think?

How will changing the concentration of the reactants affect the rate of a chemical reaction?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

All chemical reactions occur at specific rates. The rate of a chemical reaction depends on several physical and chemical factors. These factors include:

| • The concentration of the reactants | • The pressure on the reaction |
| --- | --- |
| • The temperature of the reaction | • The presence of a catalyst |

In this activity you will determine the effect of changes in concentration on the rate of a chemical reaction. The chemical reaction under investigation is the conversion of 2-butanol to methyl ethyl ketone or 2-butanone. The reaction will be monitored by using a Colorimeter to measure the change in optical density (absorbance) at 635 nm (wavelength of red light).

The equation for the reaction is:

or

permanganate ion  +  hydrogen ion  +  2 butanol  ==>  2 butanone

or

2 MnO4-  +  6  H+  +  5  C4H10O  ==>  5  C4H8O  +  8 H2O +  2  Mn2+

In order to determine the effect of concentration on the rate of the reaction, you will follow the reaction by using the Colorimeter to monitor the absorption of the manganese ion. As the reaction produces the Mn2+ the light from the Colorimeter will be absorbed.  The amount of absorption is directly related to the concentration of the manganous ion in the solution.

The rate of this chemical reaction is given by the equation:

Rate = k [reactant]a [reactant]b [reactant]c

The letters a, b and c seen as exponents are numerals which can only be determined experimentally. Each reactant must be varied separately while the other is kept constant. The effect on the rate of the reaction is noted and the value of the exponent is determined in this way:

•	If a change in concentration of one of the reactants has no effect, the exponent is 0.

•	If doubling the concentration doubles the rate, the exponent is 1.

•	If doubling the concentration quadruples the rate, the exponent is 2.

The over all order of the reaction is determined by adding a + b + c.

| SAFETY REMINDERS Wear protective gear. Follow directions for using the equipment. Handle and dispose of all chemicals and solutions properly. |  |  |  |
| --- | --- | --- | --- |

CAUTION: Never pipette by mouth. Always use a pipette bulb or a pipette pump. Be careful when handling any acid or base solutions.

## For You To Do

Use the Colorimeter to measure the change in absorbance of light by a solution of 2-butanol, potassium permangante, and sulfuric acid as the three components react. Begin with a mixture with specific concentrations of the three components, and then test mixtures with different concentrations of one component or the other. Use DataStudio or ScienceWorkshop to record and display the data. Use the data to determine the overall order of the rate of reaction.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

•	The sensor’s connector cable has a mini-DIN plug at one end and a regular DIN plug at the other.

2.	Plug the mini-DIN end of the cable into the sensor and then connect the other end of the cable into Analog Channel A on the interface.

•	The Colorimeter will automatically turn itself on when it is connected to the ScienceWorkshop interface.

3.	Open the file titled as shown;

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| C15 Reaction Rate 2.DS | C15 Reaction Rate 1 | C15_REA2.SWS |

•	The DataStudio file has a Graph display. Read the Workbook display for more information.

•	The ScienceWorkshop document has a Graph display with absorbance of light versus time.

•	Data recording is set at ten measurements per second (10 Hz).

## PART II: Sensor Calibration and Equipment Setup

### About the Colorimeter

The Colorimeter analyzes colors of light that pass through a solution. The solution is put into a rectangular container called a cuvette, which is then placed inside the Colorimeter. The measure of the amount of light that passes through a solution is called “transmittance”. Transmittance is a ratio of the intensity of the transmitted light to the intensity of the original light, and is usually expressed as a percentage.

Absorbance is related to transmittance. The light absorbed by a solution depends on the absorbing ability of the solution, the distance traveled by the light through the solution, and the concentration of the solution. The relationship of absorbance to transmittance is:

### Calibration

The general method for calibrating the Colorimeter is as follows:

•	First, calibrate the Colorimeter with a clear cuvette containing distilled water.

•	Second, calibrate the software (either DataStudio or ScienceWorkshop) for one of the four colors of light that can be selected in the Colorimeter. (For this activity you will use the RED wavelength.)

Note: The cuvette has two clear sides and two ridged sides.

•	All cuvettes should be wiped clean and dry on the outside with a tissue.

•	Handle cuvettes only by the top edge of the ridged sides.

•	All solutions should be free of bubbles.

•	Always position the cuvette so the light beam will pass through the clear sides.

### Calibrate the Colorimeter

When the Colorimeter comes on, the liquid crystal display (LCD) should say “Please calibrate”.

To calibrate the Colorimeter with a clear cuvette, fill a clean cuvette with distilled water and cap the cuvette. (The clear cuvette is a control or ‘reference’ that accounts for the small amount of light scattered or reflected by the walls of the cuvette.)

On the Colorimeter, press the ‘Select’ button () and the ‘Start/Stop’ button () at the same time.

The Colorimeter’s LCD will say “Insert reference then push SELECT”.

Place the closed cuvette inside the Colorimeter. Make sure that the clear sides of the cuvette (without ridges) are lined up with the light path in the Colorimeter. Close the lid on the Colorimeter.

On the Colorimeter, press the ‘Select’ button.

The Colorimeter will automatically calibrate itself for all four wavelengths assuming that the light passing through the clear cuvette represents “100% Transmittance”. (The automatic calibration takes only a few seconds.)

The Colorimeter’s LCD will say “CAL done, push SELECT or START”.

### Calibrate the Software

Follow these steps to calibrate the software for one of the four colors of light:

1.	Leave the cuvette with distilled water inside the Colorimeter.

2.	In the Experiment Setup window, double-click the Colorimeter icon.

•	In DataStudio, the Sensor Properties window will open. Click the ‘Calibration’ tab. In ScienceWorkshop, the Sensor Setup window will open.

3.	Select the color of light.

•	NOTE: The default color is RED, so you do not need to change the selection for this activity.

4.	Calibrate the software.

•	First, press the ‘Start/Stop’ button () to start the Colorimeter. (The LCD shows the color and wavelength, the percent transmittance, and “RUN”.)

•	Second, check the voltage under ‘Current Reading’ in DataStudio or next to ‘Cur Value:’ in ScienceWorkshop.

•	Third, when the voltage stabilizes, click the ‘Take Reading’ button under ‘High Point’ in DataStudio or the ‘Read’ button in the row for ‘High Value:’ in ScienceWorkshop.

•	Fourth, press the ‘Start/Stop’ button to stop the Colorimeter. (The LCD changes to “STOP”.)

5.	Click ‘OK’ to return to the Experiment Setup window.

•	The software is now calibrated for the Colorimeter.

### Equipment Setup

When the reactants are mixed, the solution gradually becomes darker. In other words, the solution absorbs more and more light (absorbance goes up).

You will test how each of the three substances (sulfuric acid (2 Molar), 2-butanol (1 Molar), and potassium permanganate (0.02 Molar)) effect the rate of reaction. You will vary the concentration of one reactant at a time by diluting it with distilled water.

Use the following protocol in each test:

1.	Add the specified amount of distilled water to the cuvette.

2.	Add the specified amount of 2-butanol to the cuvette.

3.	Add the specified amount of sulfuric acid to the cuvette.

4.	Add the specified amount of potassium permanganate to the cuvette LAST and quickly cap the cuvette.

5.	Quickly invert the cuvette to mix the components.

6.	Quickly put the cuvette into the Colorimeter.

7.	Start the Colorimeter, record data, then stop the Colorimeter

8.	Remove the cuvette, discard the solution, and rinse the cuvette thoroughly.

## PART IIIA: Data Recording - Vary the Concentration of Permanganate Ion

You will test three solutions made up of different amounts of the reactants as follows:

### Table IIIA: Vary the Concentration of Permanganate Ion

| Trial# | Water | 2-butanol, 2 M | Sulfuric acid, 1 M | Potassium permanganate, 0.2 M |
| --- | --- | --- | --- | --- |
| 1 | 0.8 mL | 0.8 mL | 0.8 mL | 0.8 mL |
| 2 | 1.2 mL | 0.8 mL | 0.8 mL | 0.4 mL |
| 3 | 1.4 mL | 0.8 mL | 0.8 mL | 0.2 mL |

1.	When you are ready to begin data recording, place distilled water, 2-butanol, and sulfuric acid in the cuvette in the amounts specified.

2.	Add the specified amount of potassium permanganate LAST. Quickly cap the cuvette, mix, and put the cuvette into the Colorimeter. Close the Colorimeter lid.

3.	Press the ‘Start/Stop’ button () to start the Colorimeter.

4.	Start recording data. (Hint: Click ‘Start’ in DataStudio or click ‘REC’ in ScienceWorkshop.)

5.	Record data for about 135 seconds and then stop recording data.

6.	Press the ‘Start/Stop’ button () to stop the Colorimeter. Empty and rinse the cuvette with distilled water.

7.	Repeat the procedure for trials 2 and 3 using the amounts of reactants shown above. Remember to add the KMnO4 last.

•	You will have three runs of data at the end of the data recording for Part IIIA.

## PART IIIB: Data Recording - Vary the Concentration of 2-Butanol

You will test three solutions made up of different amounts of the reactants as follows:

### Table IIIB: Vary the Concentration of 2-Butanol

| Trial# | Water | 2-butanol, 2 M | Sulfuric acid, 1 M | Potassium permanganate, 0.2 M |
| --- | --- | --- | --- | --- |
| 4 | 0.8 mL | 0.8 mL | 0.8 mL | 0.8 mL |
| 5 | 1.2 mL | 0.4 mL | 0.8 mL | 0.8 mL |
| 6 | 1.4 mL | 0.2 mL | 0.8 mL | 0.8 mL |

1.	When you are ready to begin data recording, place distilled water, 2-butanol, and sulfuric acid in the cuvette in the amounts specified.

2.	Add the specified amount of potassium permanganate LAST. Quickly cap the cuvette, mix, and put the cuvette into the Colorimeter. Close the Colorimeter lid.

3.	Press the ‘Start/Stop’ button () to start the Colorimeter.

4.	Start recording data. (Hint: Click ‘Start’ in DataStudio or click ‘REC’ in ScienceWorkshop.)

5.	Record data for about 135 seconds and then stop recording data.

6.	Press the ‘Start/Stop’ button () to stop the Colorimeter. Empty and rinse the cuvette with distilled water.

7.	Repeat the procedure for trials 5 and 6 using the amounts of reactants shown above. Remember to add the KMnO4 last.

•	You will have three more runs of data at the end of the data recording for Part IIIB.

## PART IIIC: Data Recording - Vary the Concentration of Sulfuric Acid

You will test three solutions made up of different amounts of the reactants as follows:

### Table IIIC: Vary the Concentration of Sulfuric Acid

| Trial# | Water | 2-butanol, 2 M | Sulfuric acid, 1 M | Potassium permanganate, 0.2 M |
| --- | --- | --- | --- | --- |
| 4 | 0.8 mL | 0.8 mL | 0.8 mL | 0.8 mL |
| 5 | 1.2 mL | 0.8 mL | 0.4 mL | 0.8 mL |
| 6 | 1.4 mL | 0.8 mL | 0.2 mL | 0.8 mL |

1.	When you are ready to begin data recording, place distilled water, 2-butanol, and sulfuric acid in the cuvette in the amounts specified.

2.	Add the specified amount of potassium permanganate LAST. Quickly cap the cuvette, mix, and put the cuvette into the Colorimeter. Close the Colorimeter lid.

3.	Press the ‘Start/Stop’ button () to start the Colorimeter.

4.	Start recording data. (Hint: Click ‘Start’ in DataStudio or click ‘REC’ in ScienceWorkshop.)

5.	Record data for about 135 seconds and then stop recording data.

6.	Press the ‘Start/Stop’ button () to stop the Colorimeter. Empty and rinse the cuvette with distilled water.

7.	Repeat the procedure for trials 5 and 6 using the amounts of reactants shown above. Remember to add the KMnO4 last.

•	You will have three more runs of data at the end of the data recording for Part IIIB.

## Analyzing the Data in DataStudio

Use the analysis tools in the Graph display to determine the rate of reaction for each solution. A procedure for doing this is as follows:

1.	Select the run to analyze.

2.	Use the cursor to select a region near the beginning the plot where the absorbance is changing.

3.	Select ‘Linear’ from the ‘Fit’ menu.

4.	Record the value of the slope (‘m’) as the rate of the reaction.

Repeat the process for each run of data.

## Analyzing the Data in ScienceWorkshop

Use the analysis tools in the Graph display to determine the rate of reaction for each solution. A procedure for doing this is as follows:

1.	Select the run to analyze.

2.	Click the ‘Statistics’ button () to open the statistics area. Rescale the display to fit the data.

3.	Use the cursor to select a region near the beginning the plot where the absorbance is changing.

4.	Click the ‘Statistics menu’ button () and select ‘Curve Fit, Linear Fit’ from the menu.

5.	Record the value of a2 as the rate of reaction.

Repeat the process for each run of data.

## Record your results in the Lab Report section.

# Lab Report - Activity C15: Rate of a Chemical Reaction 2

## What Do You Think?

How will changing the concentrations of the reactants affect the rate of a chemical reaction?

## Data Table

| Trial # | Variable | Amount (mL) | Rate |
| --- | --- | --- | --- |
| 1 | Potassium permanganate (KmnO4) | 0.8 |  |
| 2 | Potassium permanganate (KmnO4) | 0.4 |  |
| 3 | Potassium permanganate (KmnO4) | 0.2 |  |
| 4 | 2-butanol | 0.8 |  |
| 5 | 2-butanol | 0.4 |  |
| 6 | 2-butanol | 0.2 |  |
| 7 | Sulfuric acid (H2SO4) | 0.8 |  |
| 8 | Sulfuric acid (H2SO4) | 0.4 |  |
| 9 | Sulfuric acid (H2SO4) | 0.2 |  |

## Questions

1.	What is the effect of varying the concentration of each of the reactants?

2.	Which of the reactants effected the rate of reaction the most?

3.	Use the information in the Data Table to determine the order of each reactant and then determine the overall rate of the reaction.

# Text boxes

Clear sides aligned with light path.