# Activity C27: Determine the Concentration of a Solution – Beer’s Law (Colorimeter)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Chemical unknown | C27 Beer’s Law.DS | C27 Beer’s Law | C27_BEER.SWS |

| Equipment Needed | Qty | Chemicals and Consumables | Qty |
| --- | --- | --- | --- |
| Colorimeter (CI-6747) | 1 | Copper sulfate, 0.4 molar | 30 mL |
| Beaker, 100 mL | 2 | Copper sulfate, unknown | 5 mL |
| Cuvette (w/sensor) | 1 | Label | 6 |
| Pipette, 10 mL | 2 | Tissue | 6 |
| Stirring rod | 1 | Water, distilled | 100 mL |
| Test tube, 25 by 150 mm | 6 |  |
| Test tube rack | 1 |  |
| Protective gear | PS |  |

## What Do You Think?

The German astronomer Wilhem Beer discovered that the absorbance of light by a solution has a linear relationship to the concentration of a substance in the solution. Can you use the relationship between absorbance and concentration to determine the concentration on an unknown solution?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

A Colorimeter sends light from a light emitting diode (LED) through a solution placed in a cuvette inside the Colorimeter. The light that passes through the solution strikes a photodiode. A higher concentration of the colored solution absorbs more light and transmits less light than a solution of lower concentration. The Colorimeter monitors the light received by the photodiode as either an absorbance or a percent transmittance value.

You can use the amount of light that penetrates the solution and strikes the photodiode to compute the absorbance of each solution. A graph of absorbance versus concentration for a series of standard solutions shows a linear relationship (see the figure). The direct relationship between absorbance and concentration for a solution is known as Beer’s law.

In Beer’s law, A is the absorbance, c is the concentration, I0 is the intensity of radiation before passage through the solution, and I is the intensity of radiation transmitted through the solution.

| SAFETY REMINDERS Wear protective gear. Follow directions for using the equipment. Handle and dispose of all chemicals and solutions properly. |  |  |  |
| --- | --- | --- | --- |

CAUTION: Never pipette by mouth. Always use a pipette bulb or a pipette pump. Be careful when handling any acid or base solutions.

## For You To Do

## Use the Colorimeter to generate a graph of absorbance versus concentration using solutions of known concentration. Then use the Colorimeter to measure the absorbance of the unknown solution. Use DataStudio or ScienceWorkshop to record and display the data. Use the graph of absorbance versus concentration that you plotted for the standard solutions to determine the concentration of the unknown solution.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect the DIN plug of the Colorimeter cable to Analog Channel A on the interface.

•	The Colorimeter will automatically turn itself on when it is connected to the ScienceWorkshop interface.

3.	Open the file titled as shown;

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| C27 Beer’s Law.DS | C27 Beer’s Law | C27_BEER.SWS |

•	The DataStudio file has a Digits display, a Table display, and a Graph display of absorbance versus concentration. Read the Workbook display for more information.

•	The ScienceWorkshop document has a Digits display, a Table display and a Graph display of absorbance versus concentration.

•	Data recording is set at one measurement per second (1 Hz). Data recording is also set so that you can manually enter the concentration of the known solutions.

## PART II: Sensor Calibration and Equipment Setup

### About the Colorimeter

The Colorimeter analyzes colors of light that pass through a solution. The solution is put into a rectangular container called a cuvette, which is then placed inside the Colorimeter. The measure of the amount of light that passes through a solution is called “transmittance”. Transmittance is a ratio of the intensity of the transmitted light to the intensity of the original light, and is usually expressed as a percentage.

Absorbance is related to transmittance. The light absorbed by a solution depends on the absorbing ability of the solution, the distance traveled by the light through the solution, and the concentration of the solution. The relationship of absorbance to transmittance is:

### Calibration

The general method for calibrating the Colorimeter is as follows:

•	First, calibrate the Colorimeter with a clear cuvette containing distilled water.

•	Second, calibrate the software (either DataStudio or ScienceWorkshop) for one of the four colors of light that can be selected in the Colorimeter. (For this activity you will use the RED wavelength.)

Note: The cuvette has two clear sides and two ridged sides.

•	All cuvettes should be wiped clean and dry on the outside with a tissue.

•	Handle cuvettes only by the top edge of the ridged sides.

•	All solutions should be free of bubbles.

•	Always position the cuvette so the light beam will pass through the clear sides.

### Calibrate the Colorimeter

When the Colorimeter comes on, the liquid crystal display (LCD) should say “Please calibrate”.

To calibrate the Colorimeter with a clear cuvette, fill a clean cuvette with distilled water and cap the cuvette. (The clear cuvette is a control or ‘reference’ that accounts for the small amount of light scattered or reflected by the walls of the cuvette.)

On the Colorimeter, press the ‘Select’ button () and the ‘Start/Stop’ button () at the same time.

The Colorimeter’s LCD will say “Insert reference then push SELECT”.

Place the closed cuvette inside the Colorimeter. Make sure that the clear sides of the cuvette (without ridges) are lined up with the light path in the Colorimeter. Close the lid on the Colorimeter.

On the Colorimeter, press the ‘Select’ button.

The Colorimeter will automatically calibrate itself for all four wavelengths assuming that the light passing through the clear cuvette represents “100% Transmittance”. (The automatic calibration takes only a few seconds.)

The Colorimeter’s LCD will say “CAL done, push SELECT or START”.

### Calibrate the Software

Follow these steps to calibrate the software for one of the four colors of light:

1.	Leave the cuvette with distilled water inside the Colorimeter.

2.	In the Experiment Setup window, double-click the Colorimeter icon.

•	In DataStudio, the Sensor Properties window will open. Click the ‘Calibration’ tab. In ScienceWorkshop, the Sensor Setup window will open.

3.	Select the color of light.

•	NOTE: The default color is RED, so you do not need to change the selection for this activity.

4.	Calibrate the software.

•	First, press the ‘Start/Stop’ button () to start the Colorimeter. (The LCD shows the color and wavelength, the percent transmittance, and “RUN”.)

•	Second, check the voltage under ‘Current Reading’ in DataStudio or next to ‘Cur Value:’ in ScienceWorkshop.

•	Third, when the voltage stabilizes, click the ‘Take Reading’ button under ‘High Point’ in DataStudio or the ‘Read’ button in the row for ‘High Value:’ in ScienceWorkshop.

•	Fourth, press the ‘Start/Stop’ button to stop the Colorimeter. (The LCD changes to “STOP”.)

5.	Click ‘OK’ to return to the Experiment Setup window.

•	The software is now calibrated for the Colorimeter.

### Equipment Setup

1.	Add about 30 mL of 0.40 Molar copper sulfate (CuSO4) stock solution to a 100-mL beaker. Add about 30 mL of distilled water to another 100-mL beaker.

2.	Label four clean, dry, test tubes 1 through 4 (the fifth solution is the beaker of 0.40 M CuSO4).

3.	Pipette 2, 4, 6, and 8 mL of 0.40 M CuSO4 solution into Test Tubes 1 through 4, respectively.

4.	With a second pipette, deliver 8, 6, 4, and 2 mL of distilled water into Test Tubes 1 through 4, respectively.

5.	Thoroughly mix each solution with a stirring rod. Clean and dry the stirring rod between stirrings.

6.	Keep the remaining 0.40 M CuSO4 in the 100-mL beaker to use in the fifth trial.

•	Volumes and concentrations for the trials are summarized below:

|  | Volume | Volume |  |
| --- | --- | --- | --- |
| Trial # | 0.40 M CuSO4 (mL) | H2O (mL) | Concentration (M) |
| 1 | 2 | 8 | 0.08 |
| 2 | 4 | 6 | 0.16 |
| 3 | 6 | 4 | 0.24 |
| 4 | 8 | 2 | 0.32 |
| 5 | ~10 | 0 | 0.40 |

7.	Empty the water from the cuvette used during calibration. Using the solution in Test Tube 1, rinse the cuvette twice with approximately 1 mL amounts of solution from the test tube, and then fill the cuvette with solution. Cap the cuvette.

8.	Wipe the outside of the cuvette with a tissue and place the cuvette in the Colorimeter. Close the lid.

## PART IIIA: Data Recording with DataStudio – Solutions with Known Concentrations

1. 	Arrange the Table display so you can see it clearly.

2.	When everything is ready, press the ‘Start/Stop’ button () on the Colorimeter and then start recording data. (Hint: Click ‘Start’ in DataStudio.)

•	In DataStudio, the ‘Start’ button changes to a ‘Keep’ button (). The Table display shows default values for Concentration.

3.	When the Absorbance value stabilizes, click ‘Keep’ to record the Absorbance value in the Table display.

4.	Press the ‘Start/Stop’ button on the Colorimeter to stop the Colorimeter. Remove the cuvette from the Colorimeter and empty the cuvette. Rinse the cuvette carefully with distilled water. Empty the water from the cuvette.

5.	Using the solution in Test Tube 2, rinse the cuvette twice with approximately 1 mL amounts and then fill the cuvette with solution from Test Tube 2. Cap the cuvette. Wipe the outside with a tissue and place the cuvette in the Colorimeter. Close the Colorimeter lid.

6.	Press the ‘Start/Stop’ button on the Colorimeter to start the Colorimeter. When the Absorbance value stabilizes, click ‘Keep’ in DataStudio to record the new Absorbance value.

7.	Continue with each of your other samples (for concentrations of 0.24, 0.32, and 0.40 respectively for solutions 3, 4, and 5).

8.	After you record the Absorbance for the last solution, stop recording data. Press the ‘Start/Stop’ button to stop the Colorimeter. Rinse the cuvette with distilled water.

## PART IIIB: Data Recording with DataStudio - Solution of Unknown Concentration

1.	Measure about 10 mL of the unknown CuSO4 into a clean, dry, test tube. Rinse the cuvette twice with approximately 1 mL amounts of the unknown solution and then fill the cuvette with the unknown solution. Cap the cuvette. Wipe the outside with a tissue and place the cuvette in the Colorimeter. Close the Colorimeter lid.

•	For this part of data recording, you will monitor the Absorbance of the unknown solution on the Digits display.

2.	Press the ‘Start/Stop’ button to start the Colorimeter. In DataStudio, click the Experiment menu and select ‘Monitor Data’.

3.	When the Absorbance value displayed in the Digits display stabilizes, record the value of Absorbance in your Data Table as the value for the unknown solution.

4.	Stop recording data. Press the ‘Start/Stop’ button to stop the Colorimeter.

5.	Discard of the solutions as directed.

## PART IIIA: Data Recording with ScienceWorkshop – Solutions with Known Concentrations

1. 	Click on the Digits display to make it active. Arrange the display so you can see it while recording data.

2.	When everything is ready, press the ‘Start/Stop’ button () to start the Colorimeter and click the ‘REC’ button to begin recording data.

•	The Keyboard Sampling window will appear.

3.	Wait for the Absorbance value displayed in the Digits display to stabilize. Then enter ‘0.08’ (the concentration of the solution in Test Tube 1) in the Concentration box for Entry # 1, and click the ‘Enter’ button ().

•	The concentration will appear in the list area of the Keyboard Sampling window and the data pair you just collected should appear on the Graph and in the Table display of Absorbance and Concentration.

4.	Press the ‘Start/Stop’ button to stop the Colorimeter. Remove the cuvette from the Colorimeter and empty the cuvette. Rinse the cuvette carefully with distilled water. Empty the water from the cuvette.

5.	Using the solution in Test Tube 2, rinse the cuvette twice with approximately 1 mL amounts and then fill the cuvette with solution from Test Tube 2. Cap the cuvette. Wipe the outside with a tissue and place the cuvette in the Colorimeter. Close the Colorimeter lid.

6.	Press the ‘Start/Stop’ button to start the Colorimeter. When the Absorbance value displayed in the Digits display stabilizes, enter the new concentration, 0.16, as before.

7.	Continue with each of your other samples entering concentrations of 0.24, 0.32, and 0.40 respectively for solutions 3, 4, and 5.

8.	Click ‘Stop Sampling’ () to end data recording for Part IIIA. The Keyboard Sampling window will automatically close. Press the ‘Start/Stop’ button to stop the Colorimeter.

## PART IIIB: Data Recording with ScienceWorkshop - Solution of Unknown Concentration

1.	Measure about 8 mL of the unknown CuSO4 into a clean, dry, test tube. Rinse the cuvette twice with approximately 1 mL amounts of the unknown solution and then fill the cuvette with the unknown solution. Cap the cuvette. Wipe the outside with a tissue and place the cuvette in the Colorimeter. Close the Colorimeter lid.

•	For this part of data recording, you will monitor the Absorbance on the Digits display.

2.	Press the ‘Start/Stop’ button to start the Colorimeter. Click the ‘MON’ button to begin monitoring the data.

•	(The Keyboard Sampling window will open. Ignore it for this part of the experiment.)

3.	When the Absorbance value displayed in the Digits display stabilizes, record the value of Absorbance in your Data Table as the value for the unknown solution.

4.	Click the ‘STOP’ button to end data monitoring. Press the ‘Start/Stop’ button to stop the Colorimeter.

5.	Discard of the solutions as directed.

## Analyzing the Data

•	Your Graph may appear something like the example below.

1.	Use the built-in analysis tools in the Graph display to determine the concentration of the unknown solution.

•	Hint: Click the ‘Smart Tool’ () in DataStudio. Click the ‘Smart Cursor’ () in ScienceWorkshop.

2.	Move the cursor/crosshair so it is on the line joining the data points. Adjust the position of the cursor/crosshair until the y-coordinate matches the Absorbance of the unknown solution.

3.	Record the x-coordinate of this point as the concentration of the unknown solution.

## Record your results in the Lab Report section.

# Lab Report - Activity C27: Determine the Concentration of a Solution – Beer’s Law

## What Do You Think?

The German astronomer Wilhem Beer discovered that the absorbance of light by a solution has a linear relationship to the concentration of a substance in the solution. Can you use the relationship between absorbance and concentration to determine the concentration on an unknown solution?

## Data Table: Beer’s Law

| Trial | Absorbance | Concentration (mol/L) |
| --- | --- | --- |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
| unknown |  |  |

| Concentration of the unknown | mol/L |
| --- | --- |

## Question

1.	What is the concentration of the unknown solution?

# Text boxes

Clear sides aligned with light path.