Memorandum –Activity M01: Design and Construct a Model Rocket

To: Space Research Team
From: Joe Venus, Space Agency Administrator
Date: 12 Sep. 2017 A.D.

Greetings,

Allow me to introduce myself. My name is Joe Venus and I am the Space Agency administrator for the Mission to Other Worlds project. Your team has been selected to perform several scientific activities related to our project. Congratulations!

Your scientific research will help us to determine the best methods and materials to use for the upcoming mission. It is important to make the most accurate measurements possible, to carefully record your data, and to make a thorough report of your results. I have the highest confidence in you.

Your first task is to design and construct a model rocket.

You will use your model in upcoming activities to determine its maximum acceleration and to test different materials that are under consideration for the hull of the spacecraft.

The next section of this Workbook is the Procedure Outline for this activity. It will give you some ideas, but, as always, if you can improve on the methods or materials, please do so. Remember, read and heed the Safety Reminders in the outline.

Refer to the Technical Manual in Appendix B of this Workbook for more detailed information on the tasks for this project.

I look forward to seeing your reports for the tasks related to this project. Please submit your reports to the project manager so the manager can forward them to me.

Thank you for your efforts. Good luck on the activities.

Yours,

Joe Venus
Space Agency Administrator

# Procedure Outline – Activity M01: Design and Construct a Model Rocket

# This is a LAB activity.

| Equipment | Qty | Consumables | Qty |
| --- | --- | --- | --- |
| Construction tools | - | Construction materials | - |
| Per Student | Qty |  |  |
| Protective gear | 1 set |  |  |

| VOCABULARY | drag | stability | thrust | weight |
| --- | --- | --- | --- | --- |

## What Do You Think

What things increase or decrease the amount of drag on a rocket when it is in a planet’s atmosphere? What things increase or decrease the amount of stability of a rocket? What must be true about the thrust of a rocket compared to its weight?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

Imagine a rocket on a launching pad, ready for take-off. The countdown goes to “Zero — Ignition”, and the engines roar to life. In order for the rocket to leave the pad, the thrust of the engines must be greater than the weight of the rocket.

As the rocket climbs through the atmosphere, its weight decreases because the engines burn fuel and send the hot gases at great speed out through the exhaust nozzles. The rocket accelerates to faster and faster speeds. At the same time, the air resistance, or drag, increases because the rocket has to push more and more air out of the way as it goes faster and faster. For the ascending portion of the flight, the thrust must be greater than the sum of the weight and the drag. Eventually the rocket gets above the thickest layers of the atmosphere, and the drag decreases.

The rocket needs stability in order to stay on course as it goes up. It has several ways to maintain stability. During the ascending portion of the flight, it has powerful gyroscopes to help keep it on course. In orbit, it can use attitude control jets to adjust its motion. During descent and landing, a spacecraft such as the Space Shuttle relies on the delta-shaped wings and vertical stabilizer to control the motion.

## Model Rocket

Your model rocket must have enough thrust to overcome its weight. It needs to have maximum stability and minimum drag.

| SAFETY REMINDERS • Use all construction tools carefully. Be particularly cautious with knives, scissors, and other sharp tools. • Wear protective gear while using the construction tools. |  |  |
| --- | --- | --- |

## Procedure Outline

1.	Create a design for your model rocket.

2.	Carefully draw and label a sketch of your design and seek approval for your design from the project manager.

3.	Modify the design as needed based on the manager’s recommendations and, once the final design is approved, construct your model.

4.	Include a sketch of your final design in your report to the administrator.

5.	Answer the questions in the Report.

## [ √ ]	Remember, for more detailed information see Appendix B

Report – Activity M01: Design and Construct a Model Rocket

NAME 	_________________________________

CLASS ____________________

DATE 	____________

## [   ] What Do You Think?

What things increase or decrease the amount of drag on a rocket when it is in a planet’s atmosphere? What things increase or decrease the amount of stability of a rocket? What must be true about the thrust of a rocket compared to its weight?

Answers will vary. See the answers to the questions.___________________________________

_____________________________________________________________________________

## [   ] Rocket Design

1.	Include a detailed sketch of your final design for your model rocket. (Attach extra sheets if necessary.)

## [   ] Questions

1.	What things increase or decrease the amount of drag on a rocket when it is in a planet’s atmosphere?

______________________________________________________________________________

______________________________________________________________________________

______________________________________________________________________________

2.	What things increase or decrease the amount of stability of a rocket?

______________________________________________________________________________

______________________________________________________________________________

______________________________________________________________________________

3.	What must be true about the thrust of a rocket compared to its weight?

______________________________________________________________________________

______________________________________________________________________________

______________________________________________________________________________

## Complete the following:

VOCABULARY

drag:

stability:

thrust:

weight:

Submit this report to your project manager as soon as possible so it can be forwarded to the Space Agency administrator.