| Procedure Outline — Activity S07: Acid Rain Adapted from Chemistry with Computers, by Dan D. Holmquist and Donald L. Volz, distributed by Vernier Software, 8565 S.W. Beaverton Hillsdale Hwy., Portland, OR 97225, (503) 297-5317. |  |  |
| --- | --- | --- |
| Equipment | Qty | Consumables | Qty |
| pH Sensor (CI-6507) | 1 | Buffer solution: high pH | 100 mL |
| Base & Support Rod (ME-9355) | 1 | Buffer solution: low pH | 100 mL |
| Beaker, 250 mL | 3 | Sodium hydrogen carbonate, solid | 5 g |
| Beaker, 100 mL | 4 | Sodium hydrogen sulfite, solid | 5 g |
| Beral-type pipette, 15 cm stem | 3 | Sodium nitrite, solid | 5 g |
| Beral-type pipette, 2 cm stem | 3 | Water, distilled | 1 L |
| Beral-type pipette with 1.0 molar HCl | 1 | Water, tap | 12 mL |
| Clamp, Buret (SE-9446) | 1 |  |  |
| Test tube, 20 x 150 mm | 1 | Per Student | Qty |
| Wash bottle | 1 | Protective gear | 1 set |

| VOCABULARY | carbonic acid | nitric acid | sulfurous acid |
| --- | --- | --- | --- |

## What Do You Think?

What is acid rain and what causes it? How much change in pH in water do different gases such as carbon dioxide and nitrogen dioxide cause? What is the pH of rainwater locally?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

| Background Water vapor in the air can combine with other gases found in the air. You may be surprised to learn that rain water is slightly acidic. One reason is that water vapor can combine with carbon dioxide gas to form carbonic acid. The natural pH value of rain water is usually between 6.0 and 6.9. Rainfall accumulates in rivers and streams causing a slight acidification. |  |
| --- | --- |

Other gases found in the air can also combine with water vapor to form “acid rain”. For example, gases in automobile exhaust and other gases given off by combustion of fossil fuels can combine with water vapor to form sulfurous acid, nitrous acid, and nitric acid.

| Carbonic acid is formed when carbon dioxide gas (CO2) dissolves in rain droplets of unpolluted air: CO2(g) + H2O(l) =====> H2CO3(aq) Nitrous acid and nitric acid result from a common air pollutant, nitrogen dioxide (NO2). Most nitrogen dioxide in our atmosphere is produced from automobile exhaust. Nitrogen dioxide gas dissolves in rain drops and forms nitrous and nitric acid: |  |
| --- | --- |

2 NO2(g) + H2O(l)  =====>  HNO2(aq) + HNO3(aq)

Sulfurous acid is produced from another air pollutant, sulfur dioxide (SO2). Most sulfur dioxide gas in the atmosphere results from burning coal containing sulfur impurities. Sulfur dioxide dissolves in rain drops and forms sulfurous acid:

SO2(g) + H2O(l)  =====>  H2SO3(aq)

If large amounts of these gases are in the air, the pH of rainwater can drop drastically. Rainfall of low pH values directly affects the aquatic life in the rivers and streams where this water accumulates. Acid rain can also cause damage to plant life.

This activity has two parts: a LAB part and an optional COLLECT part. In the lab you will use a pH Sensor to measure the change in the pH in some water as the water absorbs different kinds of gases such as carbon dioxide, nitrogen dioxide, and sulfur dioxide. In the optional part of this activity, you will collect rainwater and measure its pH.

| SAFETY REMINDERS (LAB) Wear protective gear while handling chemicals. Follow directions for using the equipment. Dispose of all chemicals and solutions properly. |  |  |  |
| --- | --- | --- | --- |
| SAFETY REMINDERS (COLLECT) Wear clothing that is appropriate for the outdoor part of this activity. |

## Procedure Outline

In the lab you will make three gas generators (one each for carbon dioxide, nitrogen dioxide, and sulfur dioxide). You will bubble the gas from your gas generators through water, and use the pH Sensor to measure the change in pH of the water as it absorbs the gas. The change in pH created by the carbon dioxide gas will be compared to the change caused by sulfur dioxide and nitrogen dioxide.

## [ √ ]	Remember, for more detailed information see Appendix A.

## [   ]	Pre-Lab: Calibrate the pH Sensor

Use three beakers (100 mL), the buffer solutions, distilled water, and the wash bottle to calibrate the pH Sensor before you use it to measure pH.

(NOTE: See Appendix A for more information about how to calibrate the pH Sensor.)

## [   ]	A. Set Up the Equipment

## Overview

Fill three Beral-type pipettes with three different compounds (sodium hydrogen carbonate, sodium hydrogen sulfite, and sodium nitrite). Each of these compounds produces a different gas when hydrochloric acid is added (carbon dioxide from the sodium hydrogen carbonate, sulfur dioxide from the sodium hydrogen sulfite, and nitrogen dioxide from the sodium nitrite).

Add a small amount of hydrochloric acid to each pipette, and transfer the gas it produces to a test tube with water and the pH Sensor in it. Use the pH Sensor to measure the change in pH as the water absorbs the gas.

### [   ]	Prepare the gas generators.

1.	Label three short-stem Beral pipettes with the formula of the solid they will contain: “NaHCO3” (for sodium hydrogen carbonate), “NaNO2” (for sodium nitrite) and “NaHSO3” (for sodium hydrogen sulfite).

2.	Label three long-stem Beral pipettes with the formula of the gas they will contain: “CO2” (for carbon dioxide), “NO2” (for nitrogen dioxide) and “SO2” (for sodium dioxide). Use the 100 mL beaker to support the pipettes.

3.	Your teacher will supply a beaker containing powdered NaHCO3 (sodium hydrogen carbonate). Squeeze the bulb of the short-stem pipette labeled “NaHCO3” to push the air out of the bulb. Place the open end of the pipette into the powdered NaHCO3. Release the bulb to draw some of the powdered NaHCO3 into the pipette. Draw the powder into the pipette until there is just enough powder to fill the curved end of the bulb of the pipette when you hold the pipette with the bulb end down (see the diagram).

4.	Repeat the previous step to fill the “NaNO2” and “NaHSO3” short-stem Beral pipettes with the corresponding powdered compounds.

| 5. Get a Beral pipette with 1.0 Molar hydrochloric acid (HCl) from your teacher. (Caution: HCl is a strong acid. Hold the pipette gently, with the stem pointing up, so that HCl drops do not escape.) Insert the narrow stem of the HCl pipette into the larger opening of the pipette with the NaHCO3 (see the diagram.) Gently squeeze the HCl pipette to add about 20 drops of HCl solution to the powdered NaHCO3. When finished, remove the HCl pipette. Gently swirl the pipette that contains NaHCO3 and HCl. |  |
| --- | --- |

Carbon dioxide gas, CO2, is generated in this pipette. Place the pipette bulb down in the 100 mL beaker to prevent spillage.

6.	Repeat this same procedure to add HCl to the pipette with the powdered NaHSO3 (sodium hydrogen sulfite). Sulfur dioxide, SO2, is generated in this pipette. Place this pipette bulb down in the 100 mL beaker to prevent spillage

7.	Repeat this procedure a third time to add HCl to the powdered NaNO2 (sodium nitrite) pipette. Nitrogen dioxide, NO2, is generated in this pipette. Return the HCl pipette to your teacher. Leave the three gas-generating pipettes in the 100 mL beaker until needed.

### [   ]	Set up the pH Sensor

8.	Attach a 20 X 150 mm test tube to the base and support rod using a clamp. Add about 4 mL of tap water to the test tube. Rinse the pH Electrode with distilled water and place the electrode into the tap water in the test tube.

### [   ]	Collect the gas

| 9. Squeeze all of the air from the bulb of the long-stem pipette labeled “CO2”. Keep the bulb completely collapsed and insert the long stem of the pipette down into the gas-generating “NaHCO3” pipette. The tip of the long-stem pipette should not touch the liquid in the “NaHCO3” pipette (see the diagram). Release the pressure on the bulb so that it draws gas up into it. Store the long-stem pipette and the “NaHCO3” pipette bulb down in the 100 mL beaker. 10. Repeat the procedure using the “NaNO2” and “NO2” pipettes and the “NaHSO3” and “SO2” pipettes. |  |
| --- | --- |

## [   ]	B. Set Up the Experiment

1.	Connect the sensor to the interface. Start DataStudio or ScienceWorkshop and open the file as follows:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| S07 Acid Rain.DS | S07 Acid Rain | S07_PH.SWS |

•	The file opens with a Digits display, a Graph display, and a Table display. Data recording is set to stop automatically at 100 seconds.

2.	Calibrate the sensor. (Remember: See Appendix A for more information.)

## [   ]	C. Do the Experiment

1.	Insert the long-stem pipette labeled “CO2” into the test tube, alongside the pH sensor, so that its tip extends into the water at the bottom of the test tube.

2.	Begin recording data. After 15 seconds, gently squeeze the bulb of the pipette so that bubbles of CO2 slowly bubble up through the solution. Use both hands to squeeze all of the gas from the bulb. Data recording automatically stops at 100 seconds.

3.	Rinse the pH Electrode thoroughly with distilled water and return it to the sensor storage solution.

4.	Discard the contents of the test tube as directed by your teacher. Rinse the test tube thoroughly with tap water.

5.	Add 4 mL of tap water to the test tube.

6.	Repeat the data recording process using NO2 gas.

7.	Repeat the data recording process using SO2 gas.

8.	When you are finished, rinse the pH Electrode with distilled water and return it to the sensor storage bottle. Dispose of the six pipettes as directed.

## [   ]	D. Analyze the Data

1.	Examine each run of data in the Table display to determine the minimum pH value and maximum pH value for the water for each gas. Record the values.

2.	For each of the three gases, calculate the change in pH and record it.

3.	Record your conclusion and answer the questions in the Report.

# Record your results in the Lab Report section.

Collect (Optional)

What is the pH of your local rainwater?

1.	Rinse all glassware with distilled water.

2.	Collect water in a rain gauge and pour the water from the rain gauge into a glass beaker.

3.	Use the pH Sensor to measure the pH of the rainwater.

4.	Examine the data and record the mean pH value.

5.	Answer the questions in the Report.

## Lab Report — Activity S07: Acid Rain

Name 	_________________________________

Class ____________________

Date 	____________

## [   ] What Do You Think?

What is acid rain and what causes it? How much change in pH in water do different gases such as carbon dioxide and nitrogen dioxide cause? What is the pH of rainwater locally?

______________________________________________________________________________

______________________________________________________________________________

______________________________________________________________________________

## [   ] Analyze the Data

1.	Use the Table display to determine the minimum pH value and maximum pH value for the water for each gas.

2.	For each of the three gases, calculate the change in pH by subtracting the minimum pH from the maximum pH.

## DATA TABLE (Acid Rain)

| Gas | Minimum pH | Maximum pH | Change in pH |
| --- | --- | --- | --- |
| carbon dioxide, CO2 |  |  |  |
| nitrogen dioxide, NO2 |  |  |  |
| sulfur dioxide, SO2 |  |  |  |

3.	Use the Graph display to see how much the pH changes for each gas.

4.	For each of the three gases, sketch the change in pH.

## [   ] Conclusion

1.	How does your hypothesis (answer to the ‘What Do You Think? Question) compare with the results?

______________________________________________________________________________

______________________________________________________________________________

______________________________________________________________________________

## [   ] Questions

1.	In this activity, which gas caused the smallest drop in pH?

______________________________________________________________________________

______________________________________________________________________________

2.	Which gas caused the largest drop in pH?

______________________________________________________________________________

______________________________________________________________________________

3.	High temperatures in the automobile engines cause nitrogen and oxygen gases from the air to react and form nitrogen oxides. What two acids in acid rain result from the nitrogen oxides found in automobile exhaust?

______________________________________________________________________________

______________________________________________________________________________

## Complete the following:

VOCABULARY

carbonic acid:

nitric acid:

sulfurous acid:

If you completed the optional COLLECT part of this activity, answer the following.

1.	What was the mean (average) pH of the rainwater you collected?

______________________________________________________________________________

______________________________________________________________________________

2.	How does the pH of the rainwater compare to the pH of the water collected from the stream?

______________________________________________________________________________

______________________________________________________________________________

3.	What factors do you think have influenced the pH of the rainwater?

______________________________________________________________________________

______________________________________________________________________________