# Activity GS02: Variation of Light Intensity – Optics
(Light Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Optics | GS02 Vary Light.DS | G02 Light Bulb Intensity | G02_BULB.SWS |

| Equipment Needed | Qty | Equipment Needed | Qty |
| --- | --- | --- | --- |
| Light Sensor (CI-6504A) | 1 | Fluorescent light source (AC) | 1 |
| Flashlight (or other DC light source) | 1 | Incandescent light source (AC) | 1 |

## What Do You Think?

The purpose of this activity is to compare the variation in intensity (brightness) of light from different kinds of light sources. One light source is a flashlight powered by batteries (direct current (DC)). Another is a fluorescent light bulb that is powered by alternating current (AC) and a third is an incandescent light bulb that is powered by AC. How does the light from a DC light source compare to light from an AC light source? How does the light from a fluorescent tube compare to the light from an incandescent bulb?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

Light bulbs convert electric energy into thermal energy and light energy. We can feel the thermal energy as heat coming from the light bulb. A flashlight bulb converts electric energy into thermal energy and light energy when moving electrons collide with the atoms of the small wire inside the flashlight bulb. A fluorescent light bulb converts electric energy when moving electrons collide with atoms of gas inside the fluorescent light bulb.

In a circuit with a flashlight bulb and a battery, the electron flow is in one direction. This type of electron flow is called direct current. Once the flashlight is turned on, the flashlight bulb shines steadily all the time that it is on.

In a circuit with a fluorescent light bulb that is connected to an electric outlet, the electron flow is back-and-forth. This type of electron flow is called alternating current. Each back-and-forth movement of electrons is called a cycle. In the United States and other countries, the alternating current from an electric outlet has sixty cycles (back-and-forth) each second.

With alternating current (AC), the fluorescent light bulb will shine when the electron flow is in one direction (to the left, for example) and will not shine while the electron flow changes direction. It will shine again when the electron flow is in the opposite direction (to the right, for example). The electrons flow in one direction or the other TWICE per cycle. In the U.S. and other countries where the alternating current has sixty cycles each second, the fluorescent light bulb turns on and off 120 times each second. Therefore, the light from a fluorescent bulb has a maximum brightness 120 times each second.

One cycle each second is called one “hertz” (pronounced like “hurts”) and one hertz is abbreviated “Hz”. The number of cycles each second is called the frequency. An alternating current that has sixty cycles each second has a frequency of 60 hertz, or 60 Hz.

Fluorescent lights blink on and off at a particular frequency. The light intensity from incandescent bulbs powered by AC fluctuates as well. The light intensity from an incandescent bulb powered by DC should not vary.

| SAFETY REMINDERS Follow directions for using the equipment. |  |
| --- | --- |

## For You To Do

In this activity, use the Light Sensor to measure the intensity of light from light bulbs powered by AC or DC. There are three parts to the activity: Part A = Fluorescent bulb, AC; Part B = Incandescent bulb, AC; and Part C = Incandescent bulb, DC.

Use DataStudio or ScienceWorkshop to monitor and display the variations, if any, in the light intensity. Compare the light intensity of fluorescent and incandescent lights powered by AC, and an incandescent light powered by DC.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect the Light Sensor cable into Analog Channel A on the interface. Connect the Light Sensor to the cable.

3.	Open the document titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| GS02 Vary Light.DS | G02 Light Bulb Intensity | G02_BULB.SWS |

- The DataStudio document has a Workbook display. Read the instructions in the Workbook.

- The ScienceWorkshop document opens with a Scope display of voltage from the Light Sensor in Channel A and a Frequency Spectrum (FFT) display for the same sensor. It also has a Digits display for the voltage from the Light Sensor.

•	The data measurement is set at 5000 Hz (set by the Sweep Speed control in the Scope display). The Frequency Spectrum (FFT) is set to 256 data points.

Remember, the Scope display is like an oscilloscope. An oscilloscope is a special instrument for measuring and showing voltage, especially the voltage from something that is changing quickly. The Scope display looks like a television screen.

The Frequency Spectrum (FFT) display is a special kind of graph. The Frequency Spectrum shows the frequency (number of cycles per second) of each part of the signal that is being measured by the ScienceWorkshop interface. The Frequency Spectrum sometimes looks like many mountain peaks. Each peak stands for the frequency of one part of the signal that is being measured.

## PART II: Sensor Calibration & Equipment Setup

- You do not need to calibrate the Light Sensor. However, you may need to adjust the sensitivity of the sensor, depending on the brightness of the light source and how close the sensor is to the source.

### Adjusting Light Sensor Sensitivity

•	The Light Sensor has a GAIN switch on the top of the sensor box. The GAIN switch selects the amount of amplification for the signal that is sent to the interface. The settings are 1, 10, and 100. The setting of 10 amplifies the signal ten times and the setting of 100 amplifies the signal one hundred times.

Try the following to become more familiar with the Light Sensor:

•	Place the Light Sensor on a table so the port on the sensor is below an overhead light. Set the GAIN switch to 1.

•	Start measuring data. Click ‘Start’ in DataStudio or click ‘MON’ in ScienceWorkshop. Move the Digits display of Input Volts so you can see it clearly.

•	Switch the GAIN to 10 and observe the value of Input Volts in the Digits display. Then switch to 100 and observe the value of Input Volts.

NOTE: The maximum voltage from the sensor is 4.9 V for any GAIN setting.

•	Cover the Light Sensor port and observe the value of Input Volts.

•	Return the GAIN setting to 10. Pick up the sensor. Observe the value of Input Volts as you move the Light Sensor closer to the overhead light source. Observe what happens when you move the Light Sensor farther from the light source.

•	Click STOP to stop measuring data.

### Equipment Setup

1.	Place the Light Sensor within a few feet of a fluorescent bulb that is powered by AC.

2.	Turn on the fluorescent bulb.

## PART IIIA: Data Recording – Fluorescent Bulb, AC

1.	Start measuring data. (Hint: In DataStudio, click the ‘Start’ button (). In ScienceWorkshop, click the ‘MON’ button.) Arrange the Scope display, the Digits display, and the Frequency Spectrum (FFT) so you can see them clearly.

•	NOTE: It is likely that you will see a value in the Digits display, and a spectrum in the Frequency Spectrum display, but nothing in the Scope display. This is because the trigger control in the Scope is on, and the trigger level may be set too low for the voltage produced by the Light Sensor.

2.	Adjust the Scope display until you see the trace of voltage from the Light Sensor:

- First, adjust the trigger level.

In DataStudio, move the small triangle (the ‘Trigger Level’ pointer) on the left side of the display up or down to the desired voltage level. In ScienceWorkshop, click in the space along the left edge of the Scope display that is above the Trigger Level pointer. When you click above or below the Trigger Level Pointer, it “jumps” to the spot you clicked. The value in the Digits display will indicate the approximate trigger level you need.

•	Second, adjust the vertical position of the trace of voltage.

In DataStudio, click the up or down arrows next to ‘Offset’. In ScienceWorkshp, click the ‘UP/DOWN Arrows’ in the right side of the Scope display.

•	Finally, adjust the Sensitivity (volts per division) if needed.

In DataStudio, click the arrows to increase or decrease the sensitivity. In ScienceWorkshop, click the Vertical Scale buttons in the right side of the Scope display.

3.	Use the Frequency Spectrum to measure the frequency of the signal from the Light Sensor. Record the value of the frequency in the Lab Report section.

•	Make the FFT display (Frequency Spectrum) active. In DataStudio, click the ‘Smart Tool’ button. In ScienceWorkshop, click the ‘Smart Cursor’ button. Move the cursor/cross-hair to the top of the first peak in the display area. In DataStudio, the frequency is the first number in the ordered pair. In ScienceWorkshop, the frequency is shown below the horizontal axis.

4.	Click the STOP button to stop monitoring data.

5.	Save the trace that is displayed on the Scope. Click the Scope to make it active.

- In DataStudio, click the ‘Transfer’ button (). The data in the Scope is automatically added to the data list.

- In ScienceWorkshop, click the ‘Data Snapshot’ button () in the right side of the Scope display. The Data Cache Information window will open. Enter appropriate information for the Long Name, Short Name, and Units. Click OK to return to the Scope.

•	The Short Name for the Data Cache will appear in the Data List in the Experiment Setup window. (NOTE: You can display and analyze the Data Cache in any display that can show recorded data such as the Graph, Table, or FFT.)

## PART IIIB: Incandescent Light – AC

Repeat the activity using an incandescent light connected to an AC power supply.

## PART IIIC: Incandescent Light – DC

Repeat the activity using a battery operated flashlight.

## Analyzing the Data

- Set up a Graph display to show data for the AC fluorescent light, AC incandescent light, and DC incandescent light.

- Hint: In DataStudio, do the following:

- Click ‘Add Display…’ from the Experiment menu.

- Select ‘Graph’ from the ‘Please Choose…’ window. Click ‘OK’.

- Click and drag ‘Data’ from the Data list to the new Graph display.

- The Graph automatically rescales to fit the data. Repeat the process for the other runs of data.

- Hint: In ScienceWorkshop, do the following:

- Click the Display Menu. Select New Graph from the Display Menu.

- In the new Graph display, click the Vertical Axis Input Menu button (). Select Data Cache, Fluorescent AC from the Input Menu.

- The Graph will show the data seen in the Scope display for the fluorescent bulb powered by AC.

- Click the Add Plot Menu button () in the lower left corner of the Graph. Select Data Cache, Incandescent AC from the Add Plot Menu.

- A new plot will be added to the Graph. It will show the data seen in the Scope display for the incandescent bulb powered by AC.

- Click the Add Plot Menu button again. Select Data Cache, Incandescent DC from the Add Plot Menu.

- A third plot will be added to the Graph.

# Use your results to answer the questions in the Lab Report section.

# Lab Report - Activity GS02: Variation of Light Intensity

## What Do You Think?

The purpose of this activity is to compare the variation in intensity (brightness) of light from different kinds of light sources. One light source is a flashlight powered by batteries (direct current (DC)). Another is a fluorescent light bulb that is powered by alternating current (AC) and a third is an incandescent light bulb that is powered by AC. How does the light from a DC light source compare to light from an AC light source? How does the light from a fluorescent tube compare to the light from an incandescent bulb?

## Data Table

| Light Source | Frequency |
| --- | --- |
| Fluorescent, AC | Hz |
| Incandescent, AC | Hz |
| Incandescent, DC | Hz |

## Questions

1.	How does the frequency of light intensity variation for the fluorescent AC bulb and the incandescent AC bulb compare to the accepted value for AC frequency?

2.	What happens to the relative brightness of a fluorescent light bulb powered by AC? How does the relative brightness of an incandescent bulb run on powered by AC differ from the fluorescent bulb?

3.	What happens to the relative brightness of a flashlight bulb powered by DC?

## Ending the Activity

•	Check with your instructor about putting away the equipment for this activity.

## Computer Shutdown

When you have finished, you have several options.

1.	You can select Quit from the File menu to end the activity.

2.	You can select Save or Save As… from the File menu to save your data for this activity and the changes you’ve made to the document.

•	The original document is “locked”, so you should give your document a new filename.

3.	If you wish to go on to the next activity, select Open… from the File menu, and find the document for the next activity.

# Text boxes

Trigger Level pointer

Trigger menu

‘Offset’ arrows

Sensitivity controls

Drag and drop ‘Data’ onto the Graph.

Light bulb

Battery

Fluorescent tube