# Activity GS06: Boyle’s Law – Gas Laws (Pressure Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Gas laws | GS06 Boyle’s Law.DS | G06 Boyle’s Law | G06_BOYL.SWS |

| Equipment Needed | Qty | Other | Qty |
| --- | --- | --- | --- |
| Pressure Sensor (CI-6532) | 1 | Glycerin | 1 mL |
| Coupling, quick-release (w/sensor) | 1 |  |  |
| Syringe (w/sensor) | 1 |  |  |
| Tubing (w/sensor) | 1 |  |  |

## What Do You Think?

What happens to the pressure in a container of air as its volume is changed while the temperature remains constant?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

Robert Boyle was an English scientist who discovered a basic fact about gasses. When a gas is inside a cylinder and a piston moves up or down in the cylinder to change the volume of the gas, something also happens to the pressure of the gas.

Boyle’s Law states that the pressure of a gas in a container is related to the volume of the gas. In other words, as the volume changes, the pressure changes. For a given amount of a gas at a fixed temperature the pressure of the gas is inversely proportional to the volume. One way to verify this is to graph the inverse of gas volume versus gas pressure.

## Prediction

Will the relationship between the volume and the pressure be a direct one or will it be something else? The shape of a graph of two quantities can tell what their relationship might be.

If the two quantities have a direct relationship, their formula might be y = ax, where a is a constant. If the two quantities have an inverse relationship, their formula might be xy = b, where b is a constant.

Here are two examples of ‘Direct Relationship’ (on the left) versus ‘Inverse Relationship’:

•	Predict what the relationship will be between pressure and volume:

prediction _____________

| SAFETY REMINDERS Wear protective gear. Follow directions for using the equipment. |  |  |  |
| --- | --- | --- | --- |

## For You To Do

Use the Pressure Sensor to measure the change in pressure of the air in a syringe as you change the volume of the air in the syringe. Use DataStudio or ScienceWorkshop to record and analyze the data. Determine the relationship of pressure to volume for the air in the syringe

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect the Pressure Sensor’s DIN plug into Analog Channel A on the interface.

3.	Open the file titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| GS06 Boyle’s Law.DS | G06 Boyle’s Law | G06_BOYL.SWS |

•	The DataStudio file has a Workbook display. Read the instructions in the Workbook.

•	The document has a Digits display of Pressure, a Graph display of Volume and Inverse Volume versus Pressure, and a Table of Pressure, Volume and Inverse Volume.

•	Data recording is set for one measurement per second. Use the keyboard to enter the volume of the air inside the syringe (in milliliters).

## PART II: Sensor Calibration and Equipment Setup

You do not need to calibrate the sensor.

1.	Put a drop of glycerin on the barb end of a quick release coupling. Put the end of the coupling into one end of a short piece (about 2.5 cm) of plastic tubing that comes with the Pressure Sensor.

2.	Put a drop of glycerin on the end of the syringe. Connect the end of the syringe to the other end of the small piece of plastic tubing.

3.	Align the quick-release coupling on one end of the plastic tubing with the pressure port of the Pressure Sensor. Push the coupling onto the port, and then turn the coupling clockwise until it clicks (about one-eighth turn).

4.	Check that the syringe and Pressure Sensor have a secure seal by adjusting the volume between 20 mL and 10 mL. It should get harder to push as the volume decreases.

5.	Adjust the volume of air in the syringe to 20.0 mL. (Note: To set the initial position of the piston in the syringe, disconnect the quick-release connector from the sensor, move the piston to the first position (20 mL), and then re-connect the quick-release connector to the sensor.)

## PART III: Data Recording (for DataStudio)

•	In DataStudio, the Table display shows values for the gas volume in the syringe (for example, 20, 18, 16 and so on).

1.	When everything is ready, start recording data. (Hint: In DataStudio, click ‘Start’).

•	In DataStudio, the ‘Start’ button changes to ‘Keep’ () and the Table display shows the value of pressure next to the first volume (20 mL).

2.	Click ‘Keep’ to record the pressure.

•	The Table display changes to show the next value of volume (18 mL).

3.	Move the piston to the 18 mL mark and click ‘Keep’ to record the pressure.

4.	Continue to move the piston to each new position and then click ‘Keep’ to record the corresponding pressure.

5.	After you record the pressure for the last volume, click ‘Stop’ () to end data recording.

6.	If time permits, repeat the procedure.

## PART III: Data Recording (for ScienceWorkshop)

1.	In ScienceWorkshop, click ‘REC’ to start recording data.

•	The Keyboard Sampling window opens.

2.	When the pressure reading stabilizes, type “20” for the volume of air in the syringe and click ‘Enter’ to record the pressure.

3.	Reduce the volume to 18 mL. Type 18 for the volume and click ‘Enter’. (Note: ScienceWorkshop will prompt you for the third volume based on the pattern of the first two volumes.)

4.	Continue reducing the volume by 2.0 mL each time, checking the pressure, and entering the new volume until your last entered volume is 10.0 mL.

5.	After you enter the last volume, click ‘Stop Sampling’ to end data recording.

6.	If time permits, repeat the procedure.

## Analyzing the Data

1.	Set up the Graph display so you can examine the plot of Volume versus Pressure and also the plot of Inverse Volume versus Pressure.

2.	Set up the Table display so you can examine the Pressure, Volume and Inverse Volume.

# Use your observations to answer the questions in the Lab Report.

## Ending the Activity

•	Check with your instructor about putting away the equipment for this activity.

### Computer Shutdown

When you have finished, you have several options.

1.	You can select Quit from the File menu to end the activity.

2.	You can select Save or Save As… from the File menu to save your data for this activity and the changes you’ve made to the document.

•	The original document is “locked”, so you should give your document a new filename.

3.	If you wish to go on to the next activity, select Open… from the File menu, and find the document for the next activity.

# Lab Report - Activity GS06: Boyle’s Law – Gas Laws

## What Do You Think?

What happens to the pressure in a container of air as its volume is changed while the temperature remains constant?

## Questions

1.	From looking at your data, do the pressure and volume seem to have a direction relationship or an inverse relationship? Does this agree with Boyle’s Law?

2.	What happened to the pressure when the volume went from 20 mL to 10 mL?

3.	What are possible sources of error or limitations in this experiment? For each one, try to decide what effect it might have on the experimental results.