# Activity GS27: Chemical Equilibrium
(Pressure Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Rate of reactions | C18 Equilibrium.DS | C19 Chemical Equilibrium | C19_CHEM.SWS |

| Equipment Needed | Qty | Equipment Needed | Qty |
| --- | --- | --- | --- |
| Pressure Sensor (CI-6532A) | 1 | Tubing (w/sensor) | 1 |
| Connector, rubber stopper (w/sensor) | 1 | Protective gear | PS |
| Coupling, quick release (w/sensor) | 1 | Chemicals and Consumables | Qty |
| Flask, 250 mL | 1 | Glycerin | 1 mL |
| Graduated cylinder | 1 | Soda water, cold | 100 mL |
| Rubber stopper, one-hole | 1 | Soda water, warm | 100 mL |

## What Do You Think?

The purpose of this activity is to find out if a system in chemical equilibrium is sensitive to temperature. For example, will cold soda water or warm soda water reach chemical equilibrium faster?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

The process of chemical equilibrium is dynamic. The term dynamic means that even though no macroscopic chemical changes are noticeable, microscopic chemical changes are occurring constantly.

In any chemical reaction, the substances that react (called the reactants) combine with each other to form products. A general reaction could be written:

A  +  B   ======>   C

The equation states that “chemical A reacts with chemical B at a set rate to produce C”. This is a kinetic reaction which proceeds in only one direction. This is not a system in equilibrium.

Suppose that chemical C breaks down at certain rate to reform chemicals A and B. This is also a reaction in only one direction so the system is not in equilibrium.

C  ======> B + A

When the two reactions are combined and the rate of the forward reaction equals the rate of the reverse reaction the two opposing reactions are said to be at equilibrium.

A +  B <=======> C

Carbonic acid decomposes to form carbon dioxide and water in the following equilibrium system:

H2CO3(aq) <=======> CO2(g)  +  H2O(aq)

carbonic acid	    carbon dioxide   water

The carbon dioxide then reacts with water to reform carbonic acid. The forward reaction occurs every time you open a soda bottle or pour soda into a glass. The carbonic acid decomposes to form the ‘fizz’ that we associate with most soft drinks.

When you cap the bottle, the carbon dioxide gas begins to re-dissolve in the soda water to reform carbonic acid. If the reverse reaction (called reformation) also takes place inside a closed container, the pressure inside the container will stop increasing. The reactions still occur at the microscopic level but there is no evidence of any macroscopic change. You will know when the carbonic acid/carbon dioxide system has reached equilibrium when there is no further change in the pressure in the soda bottle.

| SAFETY REMINDERS Wear protective gear. Follow directions for using the equipment. Handle and dispose of all chemicals and solutions properly. |  |  |  |
| --- | --- | --- | --- |

## For You To Do

Use the Pressure Sensor to measure the change in pressure inside a rigid container as a small amount of soda water decomposes. Use DataStudio or ScienceWorkshop to record and display the data. Compare the data collected for cold soda water to the data collected for warm soda water.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect the Pressure Sensor’s DIN plug into Analog Channel A on the interface.

3.	Open the file titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| C18 Equilibrium.DS | C19 Chemical Equilibrium | C19_CHEM.SWS |

•	The DataStudio file has a Graph display of pressure versus time. Read the instructions in the Workbook display.

•	The ScienceWorkshop document has a Graph display of pressure versus time.

•	Data recording is set for one measurement per second.

## PART II: Sensor Calibration and Equipment Setup

### You do not need to calibrate the sensor.

### Set Up the Equipment

•	For this part you will need the following: glycerin, quick-release coupling, connector, plastic tubing, rubber stopper, flask, graduated cylinder, and warm (room temperature) soda water.

1.	Put a drop of glycerin on the barb end of a quick release coupling. Put the end of the quick release coupling into one end of a piece of plastic tubing (about 15 cm) that comes with the Pressure Sensor.

2.	Put a drop of glycerin on the barb end of the connector. Push the barb end of the connector into the other end of the plastic tubing.

3.	Fit the end of the connector into the one-hole rubber stopper.

4.	Put 100 mL of warm (room temperature) soda water in the flask.

## PART IIIA: Data Recording – Warm Soda Water

1.	Put the rubber stopper firmly into the top of the flask.

2.	Align the quick-release coupling on the end of the plastic tubing with the pressure port of the Pressure Sensor. Push the coupling onto the port, and then turn the coupling clockwise until it clicks (about one-eighth turn).

3.	When everything is ready, begin data recording. (Hint: Click ‘Start’ in DataStudio or ‘REC’ in ScienceWorkshop.)

### What do you predict the graph of pressure versus time will look like?

•	Observe the change in pressure as the carbonic acid decomposes in the flask.

4.	Continue collecting data for about 6 minutes and then stop recording data.

5.	Slowly remove the rubber stopper from the bottle. Disconnect the quick-release coupling from the Pressure Sensor.

6.	Dispose of the soda water. Rinse the flask with cold water.

## PART IIIB: Data Recording – Cold Soda Water

1.	Put 100 mL of cold soda water in the flask. Put the rubber stopper firmly into the top of the flask.

2.	Align the quick-release coupling on the end of the plastic tubing with the pressure port of the Pressure Sensor. Push the coupling onto the port, and then turn the coupling clockwise until it clicks (about one-eighth turn).

3.	When everything is ready, begin data recording.

### How will the graph of the cold soda water differ from the graph of the room temperature soda water?

4.	Continue collecting data for about 6 minutes and then stop recording data.

5.	Slowly remove the rubber stopper from the bottle. Disconnect the quick-release coupling from the Pressure Sensor.

6.	Dispose of the soda water. Rinse the flask.

## Analyzing the Data

- Use the built-in statistics tools in the Graph display to find the minimum and maximum values for pressure for each run of data.

•	Hint: In DataStudio, click the ‘Statistics menu’ button () in the display toolbar. The legend in the Graph display will show the minimum and maximum pressure.

•	Hint: In ScienceWorkshop, click the ‘Statistics’ button () to open the statistics area. Click the ‘Statistics menu’ button () in the statistics area and select Minimum and Maximum from the menu.

2.	Record the values in the Lab Report section.

3.	Use the built-in analysis tools in the Graph display to find the slope of the pressure versus time.

•	Hint: In DataStudio, use the cursor to select a region of the plot of pressure. Click the ‘Fit menu’ button () in the display toolbar and select ‘Linear’ from the menu.

•	Hint: In ScienceWorkshop, use the cursor to select a region of the plot of pressure. Click the ‘Statistics menu’ button in the statistics area and select ‘Curve Fit, Linear Fit’ from the menu.

4.	Record the slope of each run of data as the rate of decomposition.

## Record your results in the Lab Report section.

## Ending the Activity

### Equipment Clean Up

•	Check with your instructor about cleaning and putting away the equipment for this activity.

•	Check with your instructor about disposing of the chemicals that you used in the activity. DO NOT pour the chemicals down the sink unless you are told it is all right to do so.

### Computer Shutdown

When you have finished, you have several options.

1.	You can select ‘Quit’ from the ‘Fil’e menu to end the activity.

2.	You can select ‘Save’ or ‘Save As…’ from the File menu to save your data for this activity. the changes you’ve made to the document.

•	The original document is “locked”, so you should give your document a new filename.

3.	If you wish to go on to the next activity, select ‘Open…’ from the ‘File’ menu, and find the document for the next activity.

# Lab Report - Activity GS27: Chemical Equilibrium

## What Do You Think?

The purpose of this activity is to find out if a system in chemical equilibrium is sensitive to temperature. For example, will cold soda water or warm soda water reach chemical equilibrium faster?

## Data Table

| Trial | Pressure (maximum) | Pressure (minimum) | Slope |
| --- | --- | --- | --- |
| Warm soda water | kPa | kPa |  |
| Cold soda water | kPa | kPa |  |

## Questions

1.	Is there a difference in the rate to reach equilibrium?

2.	What is the relationship of temperature to the rate to reach equilibrium?

3.	Explain what is happening on a molecular level.