Twenty-Two Cent Battery

| Equipment Needed | Consumables |
| --- | --- |
| • ScienceWorkshop® Interface | • copper wire (60 cm) |
| • Voltage Sensor | • sandpaper, fine grit table |
|  | • heavy watercolor paper or thick paper towel |
|  | • salt and water solution |
|  | • 2 dimes and 2 pennies, with holes for wires |

Purpose

The purpose of this activity is to use the Voltage Sensor to measure the voltage produced by a coin ibattery,” and then compare this to the voltage of an actual D-cell battery.

Procedure

|  | Turn on the interface box and the computer. Plug a Voltage Sensor into analog channel A of the interface box. |
| --- | --- |
|  | Open the Experiment Library template file: |
| ScienceWorkshop | DataStudio( |
| MSS29 | MSS29 Cent Battery.ds |
|  | Make sure you have the correct, color-coded alligator clips on the ends of the Voltage Sensor wire leads. These clips will connect to the free ends of the copper wire. |
|  | Clean each of the coins thoroughly by sanding them with fine sandpaper. They should be shiny on all surfaces. Wash them with soap and water, then rinse and dry them. |
|  | Attach a 5 cm piece of copper wire securely to each coin, as shown in the diagram. |
|  | Cut watercolor paper (or heavy paper towel) into three round pieces, each slightly larger than a penny. Soak these pieces of paper in salt water. |
|  | Arrange a “sandwich” of pennies, dimes, and wet paper, as shown in the diagram. Stack the layers on top of each other. |
|  | Attach the wires from the dimes to another 10-cm piece of copper wire. These wires will attach to the alligator clips of the Voltage Sensor. |
|  | Connect the alligator clips of the Voltage Sensor to the wires leading from the two pennies and the two dimes. Begin recording data on the voltage created by your 22-cent battery. |
|  | Record voltage data for 60 seconds, and then stop recording data. |
|  | Re-scale the graph, and use the Smart Cursor or Smart Tool to investigate interesting areas of your data. |
|  | Compare the voltage produced by the battery you made from coins and salt water-soaked paper, to the voltage produced by an actual D-cell. |
|  | What changes could you make in your 22-cent battery that would affect the amount of voltage it produces? Why is salt water used instead of tap water? |
|  | Be sure to follow your teacher’s instructions for putting away your equipment and shutting down the computer. If you are saving your data on a disk, remember to give it a new file name. |