# Activity P29: Electrostatic Charge

# (Charge Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Electrostatics | P29 Charge.ds | (See end of activity) | (See end of activity) |

| Equipment Needed | Qty | Equipment Needed | Qty |
| --- | --- | --- | --- |
| Charge Sensor (CI-6555) | 1 | Faraday Ice Pail (ES-9042A) | 1 |
| Charge Producers (ES-9057A) | 1 set |  |  |

## What Do You Think?

The purpose of this activity is to investigate the nature of charging an object by contact as compared to charging by induction. How does the charging of an object by contact compare to the charging of an object by induction?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

Electrostatics is the study of electrical charges and their characteristics. To experimentally investigate electrostatics, some charge-detecting or measuring device is needed. The most common instrument for this purpose is the electroscope, a device with two thin gold leaves vertically suspended from a common point. When a charged object is brought near the electroscope, the gold leaves separate, roughly indicating the magnitude of the charge.

Although there are many different versions of the electroscope, all such instruments depend upon the repulsion of like charges to produce an output or reading. Unfortunately, such devices are relatively insensitive (large amounts of charge are needed to make the gold leaves separate), and the device does not have a quantitative reading.

The Charge Sensor is somewhat like an ‘electronic electroscope’. In addition to providing a quantitative measurement, the Charge Sensor is more sensitive and indicates polarity directly.

| SAFETY REMINDER Follow all safety instructions. |  |
| --- | --- |

## For You To Do

Use a Charge Sensor to determine the polarity of the Charge Producers. Then measure the amount of charge transferred to a ‘Faraday Ice Pail’ by contact with each kind of Charge Producer. Finally, use the Charge Sensor to measure the charge on the ‘Faraday Ice Pail’ that is caused by induction. Use DataStudio or ScienceWorkshop to record and display the data.

Compare charging by contact to charging by induction.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and then turn on the computer.

2.	Connect the Charge Sensor directly into Analog Channel A on the interface.

3.	Connect the cable assembly to the BNC port on the sensor. Line up the connector on the end of the cable with the pin on the BNC port. Push the connector onto the port and then twist the connector clockwise about one-quarter turn until it clicks into place.

4.	Open the file titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| P29 Charge.ds | (See end of activity) | (See end of activity) |

- The DataStudio file has a Workbook display. Read the instructions in the Workbook. The file has a Graph display and a Meter display.

•	Data recording is set at 10 samples per second (10 Hz).

•	See the pages at the end of this activity for information about creating a ScienceWorkshop file.

## PART II: Sensor Calibration and Equipment Setup

•	You do not need to calibrate the sensor for this activity.

1.	Connect the alligator clips of the sensor’s cable assembly to the inner and outer baskets of the Faraday Ice Pail.

### Preparing to Record Data

Before starting any experiment using the ‘Faraday Ice Pail’, the pail must be momentarily grounded. To ground the pail, touch the inner pail and the shield at the same time with the finger of one hand.

## PART IIIA: Data Recording – Determine the Polarity of the Charge Producers

1.	Ground the ‘Ice Pail’ and press the ‘ZERO’ button on the Charge Sensor to discharge the sensor.

2.	Start recording data. (Hint: Click ‘Start’ in DataStudio or ‘REC’ in ScienceWorkshop.)

3.	Briskly rub the blue and white surfaces of the Charge Producers together several times.

•	Without touching the ‘Ice Pail’, lower the white Charge Producer into the ‘Ice Pail’. Watch the Meter and Graph displays.

•	Remove the white Charge Producer and then lower the blue Charge Producer into the ‘Ice Pail’. Watch the results.

4.	After a few moments, stop recording data.

## PART IIIB: Data Recording – Charge on the White Charge Producer

1.	Ground the ‘Ice Pail’ and press the ‘ZERO’ button on the Charge Sensor to discharge the sensor.

2.	Start recording data.

3.	Briskly rub the blue and white surfaces of the Charge Producers together several times.

•	Lower the white Charge Producer into the ‘Ice Pail’. Rub the surface of the white Charge Producer against the inner pail and then remove the Charge Producer. Watch the Meter and Graph displays.

4.	After a few moments, stop recording data.

## PART IIIC: Data Recording – Charge on the Blue Charge Producer

1.	Ground the ‘Ice Pail’ and press the ‘ZERO’ button on the Charge Sensor to discharge the sensor.

2.	Start recording data.

3.	Briskly rub the blue and white surfaces of the Charge Producers together several times.

•	Lower the blue Charge Producer into the ‘Ice Pail’. Rub the surface of the blue Charge Producer against the inner pail and then remove the Charge Producer. Watch the Meter and Graph displays.

4.	After a few moments, stop recording data.

## PART IIID: Data Recording – Charge by Induction

1.	Ground the ‘Ice Pail’ and press the ‘ZERO’ button on the Charge Sensor to discharge the sensor.

2.	Start recording data.

3.	Briskly rub the blue and white surfaces of the Charge Producers together several times.

•	Without touching the ‘Ice Pail’ with the Charge Producer, lower the white Charge Producer into the ‘Ice Pail’.

•	While the Charge Producer is still inside the inner pail, use the finger of one hand to momentarily ground the ‘Ice Pail’. Watch the results.

•	After you ground the ‘Ice Pail’, remove your hand and then remove the Charge Producer.

4.	After a few moments, stop recording data.

5.	Ground the ‘Ice Pail’ and zero the sensor and repeat the procedure using the blue Charge Producer.

## Analyzing the Data

Use your observations and the Graph of your data to answer the questions in the Lab Report.

# Record your results in the Lab Report section.

# Lab Report - Activity P29: Electrostatic Charge

## What Do You Think?

The purpose of this activity is to investigate the nature of charging an object by contact as compared to charging by induction. How does the charging of an object by contact compare to the charging of an object by induction?

## Questions

1.	What polarity is the white Charge Producer? What polarity is the blue Charge Producer?

2.	What happens to the charge on the ‘Ice Pail’ when you rub the inner pail with the white Charge Producer and then remove the Charge Producer?

3.	What happens to the charge on the ‘Ice Pail’ when you rub the inner pail with the blue Charge Producer and then remove the Charge Producer?

4.	What happens to the charge on the ‘Ice Pail’ when the white Charge Producer is lowered into the inner pail without touching the inner pail?

5.	What happens to the charge on the ‘Ice Pail’ when the ‘Ice Pail’ is momentarily grounded while the Charge Producer is still inside the inner pail?

6.	What happens to the charge on the ‘Ice Pail’ after the Charge Producer is removed from the inner pail?

7.	How does the result of charging by contact differ from the result of charging by induction?

## Appendix: Modify a ScienceWorkshop File

Create a ScienceWorkshop file to measure the charge on a ‘Faraday Ice Pail’.

### Set Up the Charge Sensor

In the Experiment Setup window, click and drag the analog sensor plug to Channel A. Select ‘Charge Sensor’ from the list of sensors. Click ‘OK’ to return to the Experiment Setup window. Result: The Charge Sensor icon appears below Channel A on the interface.

### Set Up the Display

In the Experiment Setup window, click and drag the Meter display icon to the Charge Sensor icon. Result: The Meter display shows ‘Voltage’.

Repeat the process. Drag the Graph display icon to the Charge Sensor icon.

Arrange the Experiment Setup window and the displays so you can see the Meter and Graph displays.