# Activity P53: Diodes Lab 1 – Properties & LED’s

# (Power Output, Voltage Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Semiconductors | P53 LED.DS | (See end of activity) | (See end of activity) |

| Equipment Needed | Qty | From AC/DC Electronics Lab (EM-8656) | Qty |
| --- | --- | --- | --- |
| Voltage Sensors (CI-6503) | 2 | Diode, 1N-4007 | 1 |
| Patch Cord (SE-9750) | 2 | Light-emitting diode (LED), red | 1 |
|  |  | Light-emitting diode (LED), yellow | 1 |
|  |  | Light-emitting diode (LED), green | 1 |
|  |  | Light-emitting diode (LED), bi-color | 1 |
|  |  | Resistor, 1 kilo-ohm (k() | 1 |
|  |  | Wire Lead, 5 inch | 1 |

## What Do You Think?

What are the properties of various types of diodes?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

A diode (or p-n junction rectifier) is an electronic device that only allows current to flow in one direction through it once a certain forward voltage is established across it. If the voltage is too low, no current flows through the diode. If the voltage is reversed, no current flows through the diode (except for a very small reverse current).

A light-emitting diode emits light as current passes through the diode in the forward direction. A red-green diode is actually two diodes connected together anti-parallel so that the red diode allows current to flow in one direction and the green diode allows current to flow in the opposite direction. Thus, if DC (direct current) is applied to the red-green diode, it will be only red or only green depending on the polarity of the applied DC voltage. But if AC (alternating current) is applied to the red-green diode (bi-color LED), the diode will repeatedly blink red then green as the current repeatedly changes direction.

A bi-color LED is an example of a Zener diode. A Zener diode allows current to flow in one direction when the forward voltage is large enough, and it allows current to flow in the opposite direction when reverse voltage (called the “breakdown” voltage) is large enough (usually a few volts).

## Overview

| SAFETY REMINDER Follow all safety instructions. |  |
| --- | --- |

There are four units in the Diode Labs. You will complete the first two units in Lab 1 (this experiment). You will complete Unit Three and Unit Four in Lab 2 (the next experiment).

In the first unit you will investigate the general properties of a diode. In the second unit you will investigate different types of diodes, including light-emitting diodes (LED’s) and a Zener diode. In the third unit you will rectify a sine wave generated by the ‘Output’ of the interface. In the last unit you will setup the basic circuitry for a power supply. Use DataStudio or ScienceWorkshop to record and analyze the data.

## Unit One – Diode Properties

## For You To Do

Use the ‘Output’ feature of the ScienceWorkshop interface to produce a voltage through a circuit with a diode and a resistor. Use one Voltage Sensor to measure the voltage drop (potential difference) across the diode. Use the other Voltage Sensor to measure the voltage drop across the resistor.

Use the built-in calculation in the software to determine the current through the resistor. Use the Graph display of current versus voltage to determine the characteristics of the diode.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect one Voltage Sensor to Analog Channel A. Connect the second Voltage Sensor to Analog Channel B.

3.	Connect banana plug patch cords into the ‘OUTPUT’ ports on the interface.

4.	Open the file titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| P53 LED 1.DS | (See end of activity) | (See end of activity) |

•	The DataStudio file has a Workbook display. Read the instructions in the Workbook. The document also has a Graph display of current in milliamperes (mA) versus voltage (V), and the Signal Generator window that controls the ‘Output’.

•	See the pages at the end of this activity for information about modifying a ScienceWorkshop file.

•	The current is a built-in calculation based on the voltage drop across a 1000 ohm (1 kΩ) resistor (as measured by the Voltage Sensor connected to Channel B).

•	The Signal Generator is set to output 5.00 volt, up-ramp AC Waveform, at 2.00 Hz.

•	Data recording is set for 500 measurements per second. Data recording stops automatically at 0.5 seconds.

## PART II: Sensor Calibration and Equipment Setup

•	You do not need to calibrate the Voltage Sensors.

1.	Connect the 1N-4007 diode (black with gray stripe at one end) between the component spring next to the top banana jack and the component spring to the left of the banana jack. Arrange the diode so the gray stripe is at the left end.

2.	Connect the 1 kΩ resistor (brown, black, red) between the component spring next to the bottom banana jack and the component spring to the left of the bottom banana jack.

3.	Connect a 5-inch wire lead between the component spring at the left end of the diode and the component spring at the left end of the 1 kΩ resistor.

4.	Put alligator clips on the banana plugs of both voltage sensors. Connect the alligator clips of the Channel A voltage sensor to the wires at both ends of the diode.

5.	Connect the alligator clips of the Channel B voltage sensor to the wires at both ends of the 1 kΩ resistor.

6.	Connect banana plug patch cords from the ‘OUTPUT’ ports of the ScienceWorkshop interface to the banana jacks on the AC/DC Electronics Lab circuit board.

## PART III: Data Recording - Diode and 1 kΩ Resistor

1.	When everything is ready, start measuring data. (Click ‘Start’ in DataStudio or ‘REC’ in ScienceWorkshop.) The Signal Generator will start automatically.

•	Data recording will end automatically after 0.5 seconds.

•	Note: If the plot rapidly increases at the beginning then levels off to zero, the diode is reversed. Turn it around and record a new set of data.

## Analyzing the Data: Diode and 1 kΩ Resistor

1.	Resize the Graph to fit the data.

- The vertical axis shows the current in milliamperes based on a calculation using the voltage drop across the 1 kΩ resistor. The horizontal axis shows Voltage across the diode.

2.	Zoom in on the region of the plot of current and voltage where the current begins to increase. Make sure the upper boundary is beyond 2 milliamperes (mA).

3.	Use the built-in analysis tools to measure the value of the turn-on voltage at the point on the plot where the current reaches 2 milliamperes.

- Hint: In DataStudio, use the ‘Smart Tool’ (). The ‘Smart Tool’ displays the coordinates of its position as you move it to any position in the Graph display. When the ‘Smart Tool’ is on a data point, the ‘y’ coordinate is the current and the ‘x’ coordinate is the voltage value at that point. In ScienceWorkshop, use the ‘Smart Cursor’.

## Unit Two – Light-Emitting Diodes

## For You To Do

Use the ‘Output’ feature of the ScienceWorkshop interface to produce a voltage through a circuit with a light-emitting diode (LED) and a resistor. Use one Voltage Sensor to measure the voltage drop (potential difference) across the LED. Use the other Voltage Sensor to measure the voltage drop across the resistor.

## PART I: Computer Setup

•	You do not need to change the computer setup.

## PART II: Sensor Calibration and Equipment Setup

1.	Prepare the red, yellow, and green LED’s by very carefully bending the wire leads so they can fit in the component springs in place of the diode you used in Unit One.

2.	Replace the diode from Unit One with the first LED (red). Arrange the first LED so the short lead (cathode) is to the left.

•	The wire lead that is connected to the cathode of the LED is slightly shorter, and has a beveled shoulder near where the wire enters the LED.

## PART IIIA: Data Recording – Light-Emitting Diodes

1.	When everything is ready, start recording data.

•	The Signal Generator will start automatically. Data recording will end automatically after 0.5 seconds.

2.	Replace the first LED (red) with the next LED (yellow).

3.	Repeat the data recording procedure with the yellow and green LED.

•	You should now have four data sets.

## Analyzing the Data: Light-Emitting Diodes

1.	Setup the Graph display to show only the data for the red LED. Resize the Graph to fit the data.

2.	Zoom in on the region of the plot of current and voltage where the current begins to increase. Make sure the upper boundary is beyond 2 milliamperes (mA).

3.	Use the built-in analysis tools to measure the value of the turn-on voltage at the point on the plot where the current reaches 2 milliamperes.

4.	Repeat the analysis process for the plot of Current versus Voltage for the yellow LED.

5.	Repeat the analysis process for the plot of Current versus Voltage for the green LED.

## PART IIIB: Data Recording - Bi-Color Diode

1.	Carefully bend the wire leads of the CLEAR (bi-color) light-emitting diode so they can fit in the component springs in place of the last diode you used in PART IIIA of this unit.

2.	Replace the green LED with the bi-color LED.

3.	When everything is ready, start recording data. The Signal Generator will start automatically.

4.	Data recording will end automatically after 0.5 seconds.

•	How does the behavior of the bi-color LED differ from the other LED’s?

## Analyzing the Data: Bi-Color Led

- Setup the Graph display to show only the data for the bi-color LED. Resize the Graph to fit the data.

2.	Zoom in on the RIGHT hand region of the plot of current and voltage where the current begins to increase. Make sure the upper boundary is beyond 2 milliamperes (mA).

3.	Use the built-in analysis tools to measure the value of the turn-on voltage at the point on the plot where the current reaches 2 milliamperes.

4.	Resize the Graph to fit the data. Zoom in on the LEFT-hand region of the plot of current and voltage where the current begins to increase. Make sure the lower boundary is below -2 milliamperes (mA).

5.	Use the built-in analysis tools to measure the value of the turn-on voltage at the point on the plot where the current reaches -2 milliamperes.

# Record your results in the Lab Report section.

# Lab Report – Activity P53: Diodes Lab 1 – Properties & LED’s

## What Do You Think?

What are the properties of various types of diodes?

## Data Table 1: Light-Emitting Diodes

| Description | Voltage (V) at 2 mA |
| --- | --- |
| Diode & 1 k( resistor |  |
| Red LED |  |
| Yellow LED |  |
| Green LED |  |

## Data Table 2: Bi-Color LED

|  | Voltage (V) at 2 mA | Voltage (V) at -2 mA |
| --- | --- | --- |
| Bi-Color LED |  |  |

## Questions

1.	In Unit One, what does the plot of Diode Current vs. Voltage mean?

2.	In Unit Two, which LED (light-emitting diode) has the lowest turn-on voltage? Which LED has the highest turn-on voltage?

3.	In Unit Two, how does the forward turn-on voltage for the Bi-Color LED compare to any of the colored LED’s? How does the reverse turn-on voltage for the Bi-Color LED compare to any of the colored LED’s?

4.	How does the behavior of the Bi-Color LED differ from the other LED’s?

## Modify an existing ScienceWorkshop file

### Open the ScienceWorkshop File

Open the file titled as shown:

| ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- |
| P46 Diodes Lab 1 | P46_DIO1.SWS |

This activity uses the ‘Output’ feature of the ScienceWorkshop 750 interface to provide the output voltage. Remove the Power Amplifier in the Experiment Setup window.

### Remove the Power Amplifier Icon

In the Experiment Setup window, click the Power Amplifier icon and press <delete> on the keyboard.

Result: A warning window opens. Click ‘OK’ to return to the setup window.

### Change the Sampling Options

Open the ‘Sampling Options’ window. Change the ‘Start’ condition to ‘None’. Change the ‘Stop’ condition from ‘Samples’ to ‘Time’. Enter ‘0.5’ as the amount of time. Click ‘OK’ to return to the Sampling Options window. Click ‘OK’ again to return to the Experiment Setup window.

# Text boxes

To Channel B

To Channel A

To Interface

Cathode-

Shorter beveled ‘shoulder’ at the top of the lead