# Activity P54: Diodes Lab 2 – Rectifier & Power Supply 
(Power Output, Voltage Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Semiconductors | P54 Rectifier.DS | (See end of activity) | (See end of activity) |

| Equipment Needed | Qty | From AC/DC Electronics Lab (EM-8656) | Qty |
| --- | --- | --- | --- |
| Voltage Sensors (CI-6503) | 2 | Capacitor, 100 microfarad | 1 |
| Patch Cord (SE-9750) | 2 | Diode, 1N-4007 | 4 |
|  |  | Light-emitting diode (LED), red | 1 |
|  |  | Resistor, 1 kilo-ohm (k() | 1 |
|  |  | Resistor, 330 ohm | 1 |
|  |  | Resistor, 10 ohm | 1 |
|  |  | Wire Lead, 5 inch | 1 |
|  |  | Wire Lead, 10 inch | 1 |

## What Do You Think?

In this activity you will explore some of the basic applications of the diode. When the activity is concluded, you will understand further the importance of filtering and rectifying alternating current. What is one example of a device that uses the diode?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

A diode (or p-n junction rectifier) is an electronic device that only allows current to flow in one direction through it once a certain forward voltage is established across it. If the voltage is too low, no current flows through the diode. If the voltage is reversed, no current flows through the diode (except for a very small reverse current).

A diode can be used to provide DC current from an AC source. In other words, the diode rectifies the AC current.

When capacitors smooth the rectified current, the diodes make up part of a power supply.

## Overview

| SAFETY REMINDER Follow all safety instructions. |  |
| --- | --- |

There are four units in the Diode Lab. You completed the first two units in Lab 1 (the previous activity). You will complete Unit Three and Unit Four in this activity. In the third unit you will rectify a sine wave generated by the ‘Output’ feature of the interface. In the fourth unit you will setup the basic circuitry for a power supply. Use DataStudio or ScienceWorkshop to record and analyze the data.

## Procedure: Unit Three – Rectify a Sine Wave

## PART IA: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect one Voltage Sensor to Analog Channel A. Connect the second Voltage Sensor to Analog Channel B.

3.	Connect two banana plug patch cords into the ‘OUTPUT’ ports on the interface.

4.	Open the document title as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| P54 Rectifier.DS | (See end of activity) | (See end of activity) |

•	The DataStudio file has a Workbook display. Read the instructions in the Workbook. The document also has a Scope display of ‘Voltage, Ch A’ and ‘Voltage, Ch B’ and the Signal Generator window that controls the ‘Output’.

•	See the pages at the end of this activity for information about modifying a ScienceWorkshop file.

•	The Signal Generator for Unit Three is set to output a 3 volt ‘Sine Wave’ at 2 Hz. The output is set to start and stop automatically when you start and stop measuring data.

## PART IIA: Sensor Calibration and Equipment Setup

•	You do not need to calibrate the Voltage Sensors.

1.	Connect the 1N-4007 diode (black with gray stripe at one end) between the component spring next to the top banana jack and the component spring to the left of the banana jack. Arrange the diode so the gray stripe is at the left end.

2.	Connect the 1 k Ω resistor (brown, black, red) between the component spring next to the bottom banana jack and the component spring to the left of the bottom banana jack.

3.	Connect a 5-inch wire lead between the component spring at the left end of the diode and the component spring at the left end of the 1 kΩ resistor.

4.	Put alligator clips on the banana plugs of both voltage sensors. Connect the alligator clips of the Channel A voltage sensor to the wires at both ends of the diode.

5.	Connect the alligator clips of the Channel B voltage sensor to the wires at both ends of the 1 kΩ resistor.

6.	Connect banana plug patch cords from the ‘OUTPUT’ ports of the ScienceWorkshop interface to the banana jacks on the AC/DC Electronics Lab circuit board.

## PART IIIA: Data Recording - Rectify a Sine Wave with a Diode

1.	Begin measuring data. (Click ‘Start’ in DataStudio or ‘MON’ in ScienceWorkshop.)

•	The channel “A” trace on the Scope display is the voltage across the diode. The channel “B” trace is the voltage across the resistor.

2.	When both traces are completely across the Scope, stop measuring data.

The following information describes how to transfer data from the Scope display.

3.	Transfer data from the Scope display so it can be analyzed.

In DataStudio, click the ‘Voltage, Ch A’ input icon and then click the ‘Transfer Data’ button (). The data from Channel A’s Scope Display transfers to the ‘Data’ list. Rename ‘Data’ as ‘Diode Voltage’.

•	Repeat the process for ‘Voltage, Ch B.’ Make sure you click on the ‘Voltage, Ch B’ input icon to make it active prior to clicking the ‘Transfer Data’ button. Rename ‘Data’ as ‘Resistor Voltage’.

In ScienceWorkshop, click the top ‘Data Snapshot’ button () in the right hand corner of the Scope display. This will open the ‘Data Cache Information’ window.

•	Enter information for the ‘Long Name’ (e.g. Diode Voltage), ‘Short Name’ (Diode V), and ‘Units’ (V), then click ‘OK’.

•	Save the data for the other trace on the Scope display. Click the middle ‘Data Snapshot’ button. Enter the needed information in the ‘Data Cache Information’ window and then click ‘OK’.

•	The short names of the data caches will appear in the Data list in the Experiment Setup window.

## Analyzing the Data: Rectify a Sine Wave with a Diode

1.	View data in a Graph display.

In DataStudio, drag the ‘Voltage, Ch A Data’ from the Data list to the Graph icon located in the Displays list.

•	Drag the ‘Voltage, Ch B Data’ from the Data list to the same graph as ‘Voltage Ch A.’

In ScienceWorkshop, select ‘New Graph’ from the ‘Display’ menu.

•	Change the input for the vertical axis of the new graph. Click the vertical axis ‘Input Menu’ button (). Select ‘Data Cache, Diode Voltage’ from the Input Menu.

•	Click the ‘Add Plot Menu’ button () at the lower left corner of the graph. Select ‘Data Cache, Resistor Voltage’ from the Add Plot Menu.

•	Scale the axes so that both plots have approximately the same scale for the vertical axis.

•	Optional: If a printer is available, select Print Active Display… from the File menu.

## PART IIIB: Data Recording - Rectify a Sine Wave with a LED

1.	Remove the diode from the component springs. Carefully place the red LED (light-emitting diode) in the component springs.

2.	Repeat the data recording procedure as in Part IIIA.

## Analyzing the Data: Rectify a Sine Wave with a LED

1.	Repeat the data analysis procedure that followed Part IIIA.

•	Optional: If a printer is available, select Print Active Display… from the File menu.

## Procedure: Unit Four – Power Supply

## PART IC: Computer Setup – Power Supply: Single Diode

1.	Remove the Voltage Sensor from Channel A of the interface.

2.	Delete the Voltage Sensor icon in the Setup window.

•	In DataStudio, click the icon of the Voltage Sensor under Channel A to highlight it. Press the <delete> key on the keyboard. Click ‘OK’ in the alert dialog window that opens.

•	In ScienceWorkshop, expand the Experiment Setup window to full size. Click the icon of the Voltage Sensor under Channel A to highlight it. Press the <delete> key on the keyboard. Click ‘OK’ in the alert dialog window that opens.

3.	Modify the Signal Generator.

•	In DataStudio , double-click ‘Output Voltage’ in the Data list. In ScienceWorkshop select ‘Signal Generator’ from the Experiment menu.)

•	Click ‘Frequency’ to highlight it. Type in ‘60’ as the new frequency, and press <enter> or <return> on the keyboard.

4.	Modify the Scope display.

•	In DataStudio, drag ‘Output Voltage’ from the Data list to the Scope display.

•	In ScienceWorkshop, click the Input Menu for ‘A’. Select ‘Output Voltage’ from the menu.

## PART IIC: Equipment Setup – Power Supply: Single Diode

1.	Replace the red LED with the 1N-4007 diode in the top component springs.

2.	Replace the 1 kΩ resistor with a 330 Ω resistor in the component springs near the bottom banana jack. The 330 Ω resistor will be the “load” resistor.

2.	Get the following items for use later in this experiment: 100 microfarad (µF) capacitor, 10 ohm resistor, three additional 1N-4007 diodes.

## PART IIIC: Data Recording – Power Supply: Single Diode

1.	Start measuring data. (Hint: Click ‘Start’ in DataStudio or click ‘MON’ in ScienceWorkshop.)

•	The ‘sinusoidal’ trace on the Scope display is the ‘Output Voltage’ from the interface. The other trace is the voltage across the resistor.

(Note: The traces of ‘Output Voltage’ and ‘Voltage, Ch B’ have been offset so both traces can be seen.)

2.	Stop measuring data.

3.	Transfer the data from the Scope display as outlined in Part IIIA for later analysis.

•	In DataStudio, click the input icon and then click the ‘Transfer Data’ button. Rename the ‘Data’ as ‘Rectified Voltage’.

•	In ScienceWorkshop, click the Data Snapshot button for the channel. Enter Data Cache Information for ‘Long Name’ (e.g. Rectified Voltage), Short Name’ (Rectify V), and ‘Units’ (V) as needed to save the data for analysis.

## PART IIID: Data Recording – Power Supply: Diode and Capacitor (Filtered Voltage)

1.	Add the 100 µF capacitor in parallel to the 330 Ω resistor. Carefully bend the leads of the capacitor so they can fit in the same component springs as the resistor. The capacitor acts as a “filter”.

2.	Start measuring data for the capacitor in parallel with the 330 ohm resistor.

•	The ‘sinusoidal’ trace on the Scope display is the ‘Output Voltage’ from the interface. The other trace is the voltage across the resistor.

3.	Stop collecting data.

4.	Transfer the data from the Scope display as outlined in Part IIIA for later analysis.

•	In DataStudio, click the input icon and then click the ‘Transfer Data’ button. Rename the ‘Data’ as ‘Filtered Voltage’.

•	In ScienceWorkshop, click the Data Snapshot button () for the channel. Enter Data Cache Information for ‘Long Name’ (Filtered Voltage), ‘Short Name’ (Filter V), and ‘Units’ (V) as needed to save the data for analysis.

## PART IIIE: Data Recording – Power Supply: Diode, Capacitor and Load

1.	Add the 10 Ω resistor in parallel with the 330 Ω resistor and the 100 µF capacitor. The 10 Ω resistor simulates a motor or small light bulb.

2.	Start measuring data.

•	The ‘sinusoidal’ trace on the Scope display is the ‘Output Voltage’ from the interface. The other trace is the voltage across the resistor.

3.	After a moment or two, stop measuring data.

4.	Capture the data from the Scope Display as outlined in Part IIIA for later analysis.

•	In DataStudio, click the input icon and then click the ‘Transfer Data’ button. Rename ‘Data’ as ‘Load Resistor’.

•	In ScienceWorkshop, click the Data Snapshot button for the channel. Enter Data Cache Information for ‘Long Name’ (Load Resistor Voltage), ‘Short Name’ (Load V), and ‘Units’ (V) as needed to save the data for analysis.

## Analyzing the Data: Power Supply: Single Diode, Parts C, D, and E

•	Optional: Select Save As… from the File menu to save your data.

1.	View the data in Graph display.

In DataStudio, drag the ‘Voltage, Ch B Data’ for the ‘Rectified Voltage’ from the Data list to the Graph icon located in the Displays list.

•	Change the ‘Layout’ of the Graph to allow the captured data to appear on separate y-axes on the same display. Double click the graph, select the tab ‘Layout’, and then select ‘Do Not Group’.

•	Drag the ‘Voltage, Ch B Data’ for ‘Filtered Voltage’ and then for ‘Load Resistor Voltage’ from the Data list to the Graph.

Note:	When you drag each of the ‘Voltage, Ch B Data’ from Data list into the Graph, make sure the rectangular indicator encompasses the entire graph and not just the y-axis.

In ScienceWorkshop, select ‘New Graph’ from the Display menu.

•	Change the vertical axis input. Click the ‘Input Menu’ button. Select Data Cache, Rectified Voltage from the Input Menu.

•	Click the ‘Add Plot Menu’ button at the lower left corner of the Graph. Select Data Cache, Filtered Voltage from the Add Plot Menu.

•	Click the ‘Add Plot Menu’ button again. Select Data Cache, Load Resistor Voltage from the Add Plot Menu.

•	Optional: If a printer is available, select Print Active Display… from the File menu.

## PART IF: Computer Setup – Power Supply, Four Diodes

•	You do not need to change the computer setup.

## PART IIF: Equipment Setup – Power Supply, Four Diodes

1.	Remove the components (resistors, diode, capacitor) from the AC/DC Electronics Lab circuit board. Leave the banana plug patch cords connected to the jacks on the board.

2.	Put the diode between the second and third component springs to the left of the top banana jack. Place the diode so the gray stripe (cathode) end is to the right (toward the banana jack).

3.	Place a second diode parallel to the first between the second and third component springs to the left of the bottom banana jack. Place the diode so the gray stripe (cathode) end is to the right (toward the banana jack).

4.	Place a third diode between the component spring at the right end of the top diode, and the component spring at the right end of the bottom diode. Place the diode so the gray stripe (cathode) is toward the bottom.

5.	Place a fourth diode between the component spring at the left end of the top diode, and the component spring at the left end of the bottom diode. Place the diode so the gray stripe (cathode) is toward the bottom.

•	The diode arrangement forms a square.

6.	Put the 330-Ω resistor diagonally between the upper left corner and the lower right corner of the square of diodes.

7.	Use a five-inch wire lead to connect a component spring next to the top banana jack and the component spring at the RIGHT end of the first diode.

8.	Use another wire lead to connect a component spring next to the bottom banana jack and the component spring at the LEFT end of the second (bottom) diode.

9.	Connect the alligator clip of the black voltage sensor lead to the component spring at the upper left corner of the diode square (called a “bridge”). Connect the alligator clip of the red voltage sensor lead to the component spring at the lower right corner of the diode bridge.

## PART IIIF: Data Recording – Power Supply, Four Diodes

1.	Start measuring data

•	The ‘sinusoidal’ trace on the Scope display is the ‘Output Voltage’ from the interface. The other trace is the voltage across the resistor.

•	Note: The traces have been offset so both traces can be seen.

2.	Stop measuring data.

3.	Transfer the data from the Scope display as outlined in Part IIIA for later analysis.

•	In DataStudio, click the input icon and then click the ‘Transfer Data’ button. Rename ‘Data’ as ‘Full Rectified’.

•	In ScienceWorkshop, click the Data Snapshot button for the channel. Enter Data Cache Information for ‘Long Name’ (Full Rectified Voltage), ‘Short Name’ (Full V), and ‘Units’ (V) as needed to save the data for analysis.

## PART IIIG: Data Recording – Power Supply, Four Diodes plus Capacitor

1.	Put the 100 µF capacitor in parallel with the 330 Ω resistor.

2.	Start measuring data.

•	The ‘sinusoidal’ trace on the Scope display is the ‘Output Voltage’ from the interface. The other trace is the voltage across the resistor.

•	Note: The traces have been offset so both traces can be seen.

3.	After a moment or two, stop measuring data.

4.	Transfer the data from the Scope display as outlined in Part IIIA for later analysis.

•	In DataStudio, click the input icon and then click the ‘Transfer Data’ button. Rename ‘Data’ as ‘Filtered Full Rectified’.

•	In ScienceWorkshop, click the Data Snapshot button for the channel. Enter Data Cache Information for ‘Long Name’ (Filtered Full Rectified Voltage), ‘Short Name’ (Filtered V), and ‘Units’ (V) as needed to save the data for analysis.

## PART IIIH: Data Recording – Power Supply, Four Diodes, Capacitor and Load

1.	Put the 10 Ω resistor in parallel with the 100 µF capacitor and the 330 Ω resistor.

2.	Start measuring data.

•	The ‘sinusoidal’ trace on the Scope display is the ‘Output Voltage’ from the interface. The other trace is the voltage across the resistor.

3.	After a moment or two, stop measuring data.

4.	Transfer the data from the Scope Display as outlined in Part IIIA for later analysis.

•	In DataStudio, click the input icon and then click the ‘Transfer Data’ button. Rename ‘Data’ as ‘Load Resistor V.

•	In ScienceWorkshop, click the Data Snapshot button for the channel. Enter Data Cache Information for ‘Long Name’ (Load Resistor Voltage), ‘Short Name’ (Load V), and ‘Units’ (V) as needed to save the data for analysis.

## Analyzing the Data: Power Supply, Four Diodes

•	Optional: Select Save As… from the File menu to save your data.

1.	View the data in Graph display.

In DataStudio, drag the ‘Voltage, Ch B Data’ for the ‘Full Rectified Voltage’ from the Data list to the Graph icon located in the Displays list.

•	Change the ‘Layout’ of the Graph to allow the captured data to appear on separate y-axes on the same display. Double click the graph, select the tab ‘Layout’, and then select ‘Do Not Group’.

•	Drag the ‘Voltage, Ch B Data’ for ‘Filtered Full Rectified Voltage’ and then for ‘Load Resistor Voltage’ from the Data list to the Graph.

Note:	When you drag each of the ‘Voltage, Ch B Data’ from Data list into the Graph, make sure the rectangular indicator encompasses the entire graph and not just the y-axis.

In ScienceWorkshop, select ‘New Graph’ from the Display menu.

•	Change the vertical axis input. Click the ‘Input Menu’ button. Select Data Cache, Full Rectified Voltage from the Input Menu.

•	Click the Add Plot Menu button at the lower left corner of the Graph. Select Data Cache, Filtered Full Rectified Voltage from the Add Plot Menu.

•	Click the Add Plot Menu button again. Select Data Cache, Load Resistor Voltage from the Add Plot Menu.

•	Optional: If a printer is available, select Print Active Display… from the File menu.

# Lab Report - Activity P54: Diodes Lab 2 – Rectifier & Power Supply

## What Do You Think?

In this activity you will explore some of the basic applications of the diode. When the activity is concluded, you will understand further the importance of filtering and rectifying alternating current. What is one example of a device that uses the diode?

## Questions

1.	In Unit Three, how do the plots of voltage across the diode and voltage across the resistor compare to a complete sine wave?

2.	Based on your previous investigate of diodes, why do the plots of voltage across the diode and voltage across the resistor from the first part of Unit Three have the shape and size they do?

3.	In Unit Three, how did the plots of voltage across the diode and voltage across the resistor change when the diode was replaced with the LED? Explain.

4.	In the first part of Unit Four, what happens to the trace of voltage across the diode when the capacitor is put in parallel with the resistor? Why is the capacitor considered to be a “filter”?

5.	In the first part of Unit Four, what happens to the trace of voltage across the diode when the 10 Ω resistor is added in parallel to the capacitor and resistor?

6.	In the second part of Unit Four, how does the trace of voltage across the resistor in the four diode bridge compare to the trace of voltage across the single diode in the first part of Unit Four?

7.	What happens to the trace of voltage across the four diode bridge when the capacitor is put in parallel with the resistor? How does the shape of this trace compare to the similar “filtered” trace in the first part of Unit Four?

8.	What happens to the trace of voltage across the four diode bridge when the 10 Ω resistor is added in parallel? How does the shape of this trace compared to the similar “load resistor voltage” trace in the first part of Unit Four?

9.	Compare the performance of the single diode circuit to the four diode bridge as far as providing a steady, constant direct current when a low resistance load is connected.

## Modify an existing ScienceWorkshop file.

### Open the ScienceWorkshop File

Open the file titled as shown:

| ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- |
| P47 Diodes Lab 2 | P47_DIO2.SWS |

This activity uses the ‘Output’ feature of the ScienceWorkshop 750 interface to provide the output voltage. Remove the Power Amplifier in the Experiment Setup window.

### Remove the Power Amplifier Icon

In the Experiment Setup window, click the Power Amplifier icon and press <delete> on the keyboard.

Result: A warning window opens. Click ‘OK’ to return to the setup window.

### Check the Scope Display

The Scope display should show voltage from ‘Analog A’ and ‘Analog B’. If not, use the Input Menu to select ‘Analog A’ for the top trace.

# Text boxes

To Channel A

To Interface

To Channel B

To Interface

black

red