# Activity P56: Transistor Lab 2 – Current Gain: 
The NPN Emitter-Follower Amplifier 
(Power Output, Voltage Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Semiconductors | P56 Emitter Follower.DS | (See end of activity) | (See end of activity) |

| Equipment Needed | Qty | From AC/DC Electronics Lab | Qty |
| --- | --- | --- | --- |
| Voltage Sensors (CI-6503) | 2 | Resistor, 1 kilo-ohm (Ω) | 1 |
| Alligator Clip Adapters (SE-9756) | 2 | Resistor, 22 kilo-ohm (Ω) | 1 |
| Patch Cord (SE-9750) | 3 | Transistor, 2N3904 | 1 |
| Power Supply, 5 V DC (SE-9720) | 1 | Wire Lead | 3 |

## (* The AC/DC Electronics Lab is EM-8656)

## What Do You Think?

What are the direct current (dc) transfer characteristics of the npn transistor?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

Background

| Transistors are the basic elements in modern electronic amplifiers of all types. In a transistor circuit, the current to the base controls the current through the collector “loop”. The voltage applied to the base is called the base bias voltage. If it is positive, electrons in the emitter are attracted onto the base. Since the base is very thin (approximately 1 micron), most of the electrons in the emitter flow across into the collector, which is maintained at a positive voltage. A relatively large current, IC, flows between collector and emitter and a much smaller current, IB, flows through the base. |  |
| --- | --- |

A small change in the base voltage due to an input signal causes a large change in the collector current and therefore a large voltage drop across the output resistor, Rload. The power dissipated by the resistor may be much larger than the power supplied to the base by its voltage source. The device functions as a power amplifier.

A transistor circuit can also amplify current. What is important for amplification (or gain) is the change in collector current for a given change in base current. Gain can be defined as the ratio of output current to input current.

| SAFETY REMINDER Follow all safety instructions. |  |
| --- | --- |

## For You To Do

In this activity, use the ‘Output’ feature of the ScienceWorkshop interface to supply an alternating voltage to the base of the npn transistor. Use the DC power supply to supply voltage to the collector of the transistor. Use one Voltage Sensor to measure the voltage drop (potential difference) across a resistor in series with the base of the transistor. Use a second Voltage Sensor to measure the voltage drop across a resistor in series with the emitter of the transistor.

Use DataStudio or ScienceWorkshop to control the ‘Output’ from the interface, record and display the output voltage across the resistor in series with the base, and record and display the input voltage across the resistor in series with the emitter. Use the program to calculate the Output Current and the Input Current and then plot Output Current vs. Input Current. Compare the output and input currents to determine the “gain”.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect one Voltage Sensor to Analog Channel A. Connect the other Voltage Sensor to Analog Channel B.

3.	Connect two banana plug patch cords into the ‘OUTPUT’ ports on the interface.

4.	Open the file titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| P56 Emitter Follower.DS | (See end of activity) | (See end of activity) |

- The DataStudio file has a Graph display and a Workbook display. Read the instructions in the Workbook. The Graph display shows Emitter Current (Channel A) versus Base Current (Channel B).

•	See the pages at the end of this activity for information about modifying a ScienceWorkshop file.

- The Signal Generator is set to output a 5.00 volt ‘Sine Wave’ at 1.00 Hz. The output is set to start and stop automatically when you start and stop measuring data.

•	Data recording is set for 500 measurements per second. Data recording stops automatically at Time = 1 second.

•	The Emitter Current (vertical axis) is calculated by dividing the voltage drop across the 1 kilo-ohm (1 kΩ) resistor (Voltage, Channel A) by the resistance. The Base Current (horizontal axis) is calculated by dividing the voltage drop across the 22 kilo-ohm (22 kΩ) resistor (Voltage, Channel B) by the resistance.

## PART II: Sensor Calibration and Equipment Setup

- You do not need to calibrate the Voltage Sensors.

1.	Insert the 2N3904 transistor into the socket on the AC/DC Electronics Lab circuit board. The transistor has a half-cylinder shape with one flat side. The socket has three holes labeled “E” (emitter), “B” (base) and “C” (collector). When held so the flat side of the transistor faces you and the wire leads point down, the left lead is the emitter, the middle lead is the base, and the right lead is the collector.

2.	Connect the 1 kΩ resistor (brown, black, red) vertically between the component spring at the left edge of the component area on the AC/DC Electronics Lab circuit board.

3.	Connect the 22 kΩ resistor (red, red, orange) vertically between the component springs to the right of the 1 k( resistor.

4.	Connect a wire lead between the component spring next to the emitter terminal of the transistor, and the component spring at the top end of the 1 kΩ resistor.

5.	Connect another wire lead between the component spring next to the base terminal of the transistor, and the component spring at the top end of the 22 kΩ resistor.

6.	Connect another wire lead between the component spring next to the collector terminal of the transistor, and the component spring next to the top banana jack.

7.	Connect a patch cord from the positive (+) terminal of the DC power supply to the top banana jack.

8.	Use an alligator clip adapter to connect a patch cord from the signal output () port of the interface to the component spring at the bottom end of the 22 kΩ resistor.

9.	Use an alligator clip adapter to connect a patch cord from the negative (or ground) terminal of the DC power supply to the component spring at the bottom end of the 1 kΩ resistor.

10.	Connect the patch cord from the ground output port () of the interface to the negative (or ground) terminal of the DC power supply.

11.	Put alligator clips on the banana plugs of both Voltage Sensors. Connect the red alligator clip of the Voltage Sensor in Analog Channel A to the component spring at the top end of the 1 k( resistor, and the black clip to the component spring at the bottom end.

12.	Connect the black alligator clip of the Voltage Sensor in Analog Channel B to the component spring at the top end of the 22 k( resistor, and the red clip to the component spring at the bottom end.

## PART III: Data Recording

1.	Turn on the DC power supply and adjust its voltage output to exactly +5 Volts.

2.	When everything is ready, start recording data. Recording stops automatically after 1 s.

3.	Turn off the DC power supply when data recording is finished.

## Analyzing The Data

•	Because the Graph displays the output or “collector” current (Ic) versus the input or “base” current (Ib), the slope of the linear region of the plot gives the current gain of the transistor.

1.	Resize the Graph to fit the data. Zoom in on the linear region of the plot.

2.	Use the built-in analysis tools to find the slope of a best-fit line applied to the linear region of the plot.

•	The slope can be interpreted as follows:

where ß is called current gain of the transistor.

3.	Determine the current gain of the 2N3904 transistor.

# Record your results in the Lab Report section.

# Lab Report – Activity P49: Transistor Lab 2 – Current Gain: 
The NPN Emitter-Follower Amplifier

## What Do You Think?

What are the direct current (dc) transfer characteristics of the npn transistor?

## Data

## current gain of the 2N3904 transistor = ________________

## Questions

1.	How does the general shape of the plot for the transistor compare to the plot of current versus voltage for a diode?

2.	What is the current gain of the 2N3904 transistor?

## Modify an existing ScienceWorkshop file.

### Open the ScienceWorkshop File

Open the file titled as shown:

| ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- |
| P49 Transistor Lab 2 | P49_TRN2.SWS |

This activity uses the ‘Output’ feature of the ScienceWorkshop 750 interface to provide the output voltage. Remove the Power Amplifier in the Experiment Setup window.

### Remove the Power Amplifier Icon

In the Experiment Setup window, click the Power Amplifier icon and press <delete> on the keyboard.

Result: A warning window opens. Click ‘OK’ to return to the setup window.

### Modify the Signal Generator

Set the Signal Generator to output a 5 volt ‘Sine Wave’ at 1 Hz.

# Text boxes

2N3904

c = collector

b = base

e = emitter

1 kΩ

22 kΩ

Transistor

To Channel A

To Channel B

To +5 V

To Output on Interface

To Ground on Power Supply