# Activity P57: Transistor Lab 3 – Common-Emitter Amplifier 
(Voltage Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Semiconductors | P57 Common Emitter.DS | (See end of activity) | (See end of activity) |

| Equipment Needed | Qty | From AC/DC Electronics Lab (EM8656) | Qty |
| --- | --- | --- | --- |
| Voltage Sensor (CI-6503) | 1 | Capacitor, 1 microfarad (µF) | 1 |
| Alligator Clip Adapters (SE-9756) | 1 | Capacitor, 10 microfarad (µF) | 1 |
| Patch Cord (SE-9750) | 4 | Resistor, 1 kΩ (brown-black-red) | 4 |
| Power Supply, 5 V DC, (SE-9720) | 1 | Resistor, 10 kΩ (brown-black-orange) | 1 |
|  |  | Resistor, 22 kΩ (red-red-orange) | 2 |
|  |  | Transistor, 2N3904 | 1 |
|  |  | Wire Lead, 10 inch | 1 |
|  |  | Wire Lead, 5 inch | 4 |

## What Do You Think?

Is it possible for a small semiconductor device to produce a larger output signal than the input signal supplied to it?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

The purpose of this activity is to investigate the voltage and current amplification characteristics of the npn transistor in a common-emitter amplifier circuit.

## Background

In the npn transistor, the current flow to the base is much smaller than the current flow to the collector. This allows the transistor to be used as an amplifier. The transistor can amplify current and voltage.

If the input voltage is small enough so that it is much smaller than the forward bias on the emitter connection, the input current will encounter small impedance. The input voltage will not need to be large in order to produce sizeable currents.

Additionally, since the output voltage across the load resistor RL is the product of the output current (collector current) and the value of RL, the output voltage can also be made large. As a result, the output voltage can be much larger than the input voltage.

The common-emitter amplifier derives its name from the fact that the base wire of the transistor and the collector wire of the transistor meet at the emitter wire; they have the emitter wire in common.

Each section of the common-emitter amplifier circuit performs a specific function. In Section 1, the Input Coupling Circuit keeps DC voltages from changing the bias circuit. The function of Section 2, the Bias Circuit, is to provide a voltage that keeps the transistor in its active region. Section 3 is the Amplifier circuit. Section 4, the Output Coupling Circuit, allows only the AC signal from the transistor to reach the load resistor so that the load resistance doesn’t affect the operating voltage.

| SAFETY REMINDER Follow all safety instructions. |  |
| --- | --- |

## For You To Do

Use the ‘Output’ feature of the ScienceWorkshop interface to supply an AC voltage to the base of the npn transistor. Use the DC power supply to supply voltage to the collector of the same transistor. Use a Voltage Sensor to measure the voltage drop (potential difference) across the 22 kΩ resistor in the Output Coupling Circuit, which is connected to the collector of the transistor.

Use DataStudio or ScienceWorkshop to record and display the voltage across the resistor in the Output Coupling Circuit as well as the ‘Output’ from the interface. Measure the voltage going to the base of the transistor and the voltage from the collector in order to calculate the output voltage. Compare the actual output voltage to the theoretical output voltage.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect one Voltage Sensor to Analog Channel A.

3.	Connect two banana plug patch cords into the ‘OUTPUT’ ports on the interface.

4.	Open the document titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| P57 Common Emitter.DS | (See end of activity) | (See end of activity) |

•	The DataStudio document has a Workbook display. Read the instructions in the Workbook. The document has a Scope display of the ‘Output Voltage’ from the interface and ‘Voltage, Ch A’ from the Voltage Sensor.

•	See the pages at the end of this activity for information about modifying a ScienceWorkshop file.

•	The Signal Generator is set to output a 0.2 volt ‘Sine Wave’ at 300 Hz. The output is set to start and stop automatically when you start and stop measuring data.

## PART II: Sensor Calibration and Equipment Setup

- You do not need to calibrate the Voltage Sensor. You will need the following components:

| Item | Quantity | Item | Quantity |
| --- | --- | --- | --- |
| 1 kΩ resistor (brown-black-red) | 4 | 10 µF capacitor | 1 |
| 10 kΩ resistor (brown-black-orange) | 1 | wire lead, five inch | 4 |
| 22 kΩ resistor (red-red-orange) | 2 | wire lead, ten inch | 1 |
| 1 µF capacitor | 1 | 2N3904 transistor | 1 |

1.	Insert the 2N3904 transistor into the socket on the AC/DC Electronics Lab circuit board. The transistor has a half-cylinder shape with one flat side. The socket has three holes labeled “E” (emitter), “B” (base) and “C” (collector). When held so the flat side of the transistor faces you and the wire leads point down, the left lead is the emitter, the middle lead is the base, and the right lead is the collector.

2.	Connect one five-inch wire lead from the component spring at the base terminal of the transistor to the component spring below the base terminal of the transistor.

3.	Connect one 1 kΩ resistor from the component spring at the bottom end of the wire lead coming from the base terminal of the transistor, to the component spring directly below (at the bottom edge of the AC/DC lab board).

4.	Connect the wire at the negative end of the 1-µF capacitor to the same component spring at the bottom edge of the AC/DC lab board. Do not connect the other wire lead of the capacitor to anything.

| • NOTE: The negative end of the 1-µF capacitor has a small round bump. |  |
| --- | --- |

5.	Connect one five inch wire lead from the component spring next to the emitter terminal of the transistor to the component spring at the top left corner of the component area of the AC/DC Electronics Lab circuit board.

6.	Connect one 1 kΩ resistor from the component spring at the top left corner of the component area and the component spring directly below.

7.	Connect one five-inch wire lead from the component spring next to the collector terminal of the transistor to the component spring to the right and slightly below.

8.	Connect one 1-kΩ resistor from the component spring at the end of the wire lead from the collector terminal, to the component spring below and slightly to the right of the component spring at the end of the wire lead from the collector terminal.

9.	Connect one 1 kΩ resistor from the component sprint to the right of the top banana jack, to the component spring directly to the left of the first component spring.

10.	Connect a patch cord from the positive (+) terminal of the DC power supply to the top banana jack on the AC/DC lab board.

11.	Connect a patch cord from the negative (-) terminal of the DC power supply to the bottom banana jack on the AC/DC lab board.

12.	Connect the ten inch wire lead from the component spring next to the bottom banana jack to the component spring at the bottom end of the 1 kΩ resistor that is connected to the emitter terminal of the transistor.

13.	Find the component spring at the end of the wire lead that is connected to the component spring at the base terminal of the transistor. Connect the 10-kΩ resistor from the component spring at the end of the wire lead to a component spring at the bottom left corner of the board.

•	NOTE: You can connect one end of the 10 kΩ resistor to the same component spring that holds one end of the ten inch wire lead.

14.	Return to the component spring that is at the end of the wire lead connected to the base terminal of the transistor. Connect one 22 kΩ resistor from the component spring at the end of the wire lead to the component spring that is to the right and below (at the edge of the AC/DC lab board).

15.	Connect one five-inch wire lead from the component spring at the end of the 22-kΩ resistor to a component spring next to the top banana jack.

16.	Put an alligator clip on one end of patch cord. Connect the alligator clip to the wire at the end of the 1 µF capacitor. Connect the other end of the patch cord to the ‘OUTPUT’ () port of the ScienceWorkshop interface.

17.	Connect a patch cord from the ground () port of the ScienceWorkshop interface to the negative terminal of the DC power supply.

18.	Put alligator clips on the banana plugs of the Voltage Sensor. Connect the alligator clip of the black wire of the Voltage Sensor to the component spring next to the bottom banana jack at the lower right corner of the AC/DC board.

19.	Twist the wire from the negative end of the 10-µF capacitor together with the wire at one end of one 22-kΩ resistor.

| • NOTE: The negative end of the 10-µF capacitor has a slight bump. The positive end has an indentation around it. There is a band on the side of the capacitor with arrows that point to the negative end. |  |
| --- | --- |

20.	Connect the wire from the positive end of the 10-µF capacitor to the component spring at one end of the wire lead connected to the collector terminal of the transistor. Connect the wire from the 22-kΩ resistor to a component spring next to the bottom banana jack at the lower right corner of the AC/DC lab board.

21.	Carefully connect the alligator clip of the red wire of the Voltage Sensor to the twisted wires of the 10-µF capacitor and the 22-kΩ resistor.

## PART III: Data Recording

- Start measuring data. (Click ‘Start’ in DataStudio or ‘MON’ in ScienceWorkshop.)

2.	Turn on the DC power supply and adjust its voltage output to exactly +5 volts.

- Observe the trace of voltage going to the base terminal of the transistor from the ‘OUTPUT’ of the interface (the trace for ‘Output Voltage’). Compare this trace to the trace of voltage measured by the Voltage Sensor connected to Channel A (Voltage, Ch A).

3.	Measure the voltages. Use the built-in analysis tools in the Scope display. (Hint: In DataStudio, click the ‘Smart Tool’ button. In ScienceWorkshop, click the ‘Smart Cursor’ button. This will stop data monitoring temporarily.)

- Move the analysis tool (‘Smart Tool’ or ‘Smart Cursor’) to the first peak of the trace for the voltage from the ‘OUTPUT’ of the interface (‘Output Voltage’). Record the voltage value for the peak. (Hint: In DataStudio, the voltage is the second number in the ordered pair. In ScienceWorkshop, the voltage is displayed next to the sensitivity controls (v/div)).

- Move the cursor/cross-hair to the first peak of the trace for the voltage for Channel A (directly below the peak of the ‘Output Voltage’ trace). Record the voltage value for the peak.

4.	Stop measuring data.

5.	Turn off the DC power supply.

# Record your results in the Lab Report section.

# Lab Report - Activity P57: Transistor Lab 3 – Common-Emitter Amplifier

## What Do You Think?

Is it possible for a small semiconductor device to produce a larger output signal than the input signal supplied to it?

## Data

Voltage (peak) of B	=           V

Voltage (peak) of A	=           V

## Analyzing the Data

1.	Use the values you recorded to calculate the ratio of input voltage (Voltage of B) to output voltage (Voltage of A).

= ___________

2.	Calculate the theoretical output voltage as follows:

= ____________

where RC is the value of the resistor in series with the collector terminal (2 kΩ), and RE is the value of the resistor in series with the emitter terminal (1 kΩ). Calculate the theoretical output voltage for the common-emitter amplifier.

## Questions

1.	What is the phase relationship between the input signal and the output signal?

- How does the actual output voltage compare to the theoretical value?

## Modify an existing ScienceWorkshop file.

### Open the ScienceWorkshop File

Open the file titled as shown:

| ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- |
| P50 Transistor Lab 3 | P50_TRN3.SWS |

This activity uses the ‘Output’ feature of the ScienceWorkshop 750 interface to provide the output voltage. Remove the Power Amplifier in the Experiment Setup window.

### Remove the Power Amplifier Icon

In the Experiment Setup window, click the Power Amplifier icon and press <delete> on the keyboard.

Result: A warning window opens. Click ‘OK’ to return to the setup window.

### Remove the Channel B Voltage Sensor

In the Experiment Setup window, click the Voltage Sensor icon under Channel B and press <delete> on the keyboard. Click ‘OK’ in the warning window to return to the setup window.

### Check the Signal Generator

Set the Signal Generator to output a 0.2 volt ‘Sine Wave’ at 300 Hz.

# Text boxes

To ‘OUTPUT’ on interface