# Activity P58: Magnetic Field of a Solenoid 
(Magnetic Field Sensor, Power Amplifier)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Magnetism | P58 Solenoid.DS | P52 Mag Field Solenoid | P52_SOLE.SWS |

| Equipment Needed | Qty | Equipment Needed | Qty |
| --- | --- | --- | --- |
| Magnetic Field Sensor (CI-6520) | 1 | Patch Cord (SE-9750) | 2 |
| Power Amplifier (CI-6552) | 1 | Solenoid (SE-8563) | 1 |
| Meter stick | 1 |  |  |

## What Do You Think?

Solenoids are an important aspect of automated controls. Solenoids are used in common household appliances. Can you name a few? (Hint: Start with the washing machine.)

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

The magnetic field inside a very long solenoid is given by:

where µo = 4 x 10-7 (tesla•meters)/amp, I is the current (amps), and n is the number of turns of wire per unit length (#/meter) of the solenoid. Notice that this expression is independent of the radius of the coil and the position inside the coil.

| SAFETY REMINDER Follow all safety instructions. |  |
| --- | --- |

## For You To Do

The goal of this laboratory activity is to measure the magnetic field inside a solenoid and compare the magnetic field to a theoretical value based on the current through the solenoid.

Use the Magnetic Field Sensor to measure the magnetic field strength inside a cylindrical solenoid. Use the Power Amplifier to provide a direct current through the solenoid.

Use DataStudio or ScienceWorkshop to record and display the magnetic field and the current through the solenoid. Compare the measured magnetic fields inside the solenoid to the theoretical magnetic field calculated on the basis of current and the number of turns of wire per unit length.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect the Magnetic Field Sensor DIN plug to Analog Channel A on the interface.

3.	Connect the Power Amplifier to Analog Channel B. Plug the power cord into the back of the Power Amplifier and connect the power cord to an appropriate electrical receptacle.

4.	Open the document titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| P58 Solenoid.DS | P52 Mag Field Solenoid | P52_SOLE.SWS |

•	The DataStudio document has a Workbook display. Read the instructions in the Workbook. It also h as a Digits display of magnetic field strength and current.

•	The ScienceWorkshop document opens with a Digits display of magnetic field strength and a Digits display of current. It also has the Signal Generator window that controls the Power Amplifier.

•	The Signal Generator is set to output DC at 10.0 V. It is set ‘Auto’ so it will start and stop automatically when you start and stop measuring data.

## PART II: Sensor Calibration & Equipment Setup

•	You do not need to calibrate the Magnetic Field Sensor or the Power Amplifier. The Magnetic Field Sensor produces a voltage that is directly proportional to the magnetic field strength as follows: 10 millivolts = 10 gauss (where 1000 gauss = 0.1 tesla). The sensor’s range is ±2000 gauss.

1.	Use only the outer coil of the Primary/Secondary Coil set. Use patch cords to connect the output of the Power Amplifier to the input jacks on the solenoid.

2.	Position the solenoid and Magnetic Field Sensor so the end of the sensor can be placed inside the solenoid.

## PART III: Data Recording

1.	Hold the Magnetic Field Sensor far away from any source of magnetic fields and zero the sensor by pushing the TARE button on the sensor box.

2.	Select the AXIAL field by clicking the RADIAL/AXIAL SELECT SWITCH on the sensor.

3.	Return the sensor to its position next to the solenoid.

4.	Start measuring data. The Signal Generator will start automatically.

5.	Record the value of current from the Digits display into the Data section.

6.	Insert the sensor rod into the center of the coil. Move the sensor around inside the coil to see if the radial position of the sensor changes the reading on the computer.

7.	Record the reading for the axial component of the magnetic field inside the coil in the middle, away from either end of the coil. Record this value in the Data section.

8.	Remove the Magnetic Field Sensor from the coil. Select the RADIAL field. Hold the sensor far away from any source of magnetic fields and re-zero the sensor by pushing the TARE button on the sensor box.

9.	Insert the sensor rod into the center of the coil. Record the reading for the radial component of the magnetic field in the Data section.

10.	Measure the length of the solenoid coil.

•	Note: When measuring the coil, make sure that you only measure the length of the solenoid with the wrapped coil and not the entire solenoid.

## Analyzing the Data

1.	Calculate the theoretical value of the magnetic field inside the coil using the measured current, length, and number of turns for the coil (for the SE-8653 outer coil, the number of turns is 2920). Record this value.

2.	Use you data to answer the questions in the Lab Report section.

# Record your results in the Lab Report section.

# Lab Report - Activity P58: Magnetic Field of a Solenoid

## What do you think?

Solenoids are an important aspect of automated controls. Solenoids are used in common household appliances. Can you name a few? (Hint: Start with the washing machine.)

## Data

Recorded Current 			= _______ amps

Length of Primary Coil 		= _______ cm

Theoretical Magnetic Field	= _______ gauss

Measured Magnetic Fields (gauss)

| Axial (gauss) | Radial (gauss) |
| --- | --- |

## Questions

1.	Did the axial reading change when the sensor was moved radially outward from the center toward the windings on the coil?

2.	Was the axial reading different from the reading in the middle of the coil when the sensor was inside but near the ends of the coil?

3.	By comparing the axial and radial readings, what can you conclude about the direction of the magnetic field lines inside a solenoid?

4.	Compare the theoretical value to the axial value using a percent difference. What are some factors that could account for this percent difference?

# Text boxes

To Power Amplifier