# Activity P59: Magnetic Field of Helmholtz Coils
(Magnetic Field Sensor, Power Amplifier, Rotary Motion Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- | --- |
| Magnetism | P59 Helmholtz Coils.DS | (See end of activity) | (See end of activity) |

| Equipment Needed | Qty | Equipment Needed | Qty |
| --- | --- | --- | --- |
| Magnetic Field Sensor (CI-6520) | 1 | Lab Jack (SE-9374) | 2 |
| Power Amplifier (CI-6552) | 1 | Mass and Hanger Set (ME-9348) | 1 |
| Rotary Motion Sensor (CI-6538) | 1 | Meter stick, wood | 1 |
| Base and Support Rod (ME-9355) | 1 | Patch Cord (SE-9750) | 3 |
| Helmholtz Coil (EM-6711) | 2 | String (SE-8050) | 1 m |

## What Do You Think?

The purpose of this activity is to examine the magnetic field produced by the current in a pair of Helmholtz coils, and to measure the magnetic field strength between the coils and compare the measured value to the theoretical value. How does the strength of the magnetic field between the coils relate to the distance of separation between the Helmholtz coils?

Take time to answer the ‘What Do You Think?’ question(s) in the Lab Report section.

## Background

Helmholtz coils are a pair of coils that each has the same radius, R. The coils are usually placed parallel to each other a distance R apart and along the same axis.

The magnetic field along the axis at the midpoint between the two coils is then given by

where µo = 4 x 10-7 (tesla•meters)/amp, I is the current (amps) in one coil, R is the radius of the coil, and N is the number of turns of wire in one coil.

| SAFETY REMINDER Follow all safety instructions. |  |
| --- | --- |

## For You To Do

In this activity, use the Power Amplifier to supply the current through the Helmholtz coils. Use the Magnetic Field Sensor to measure the strength of the magnetic field between the coils. Use the Rotary Motion Sensor to measure the position of the Magnetic Field Sensor as you move it along the axis of the two coils.

Use DataStudio or ScienceWorkshop to control the Power Amplifier and measure and display the strength of the magnetic field and the position of the sensor. Compare the measured magnetic field strength to the theoretical magnetic field strength. Determine the relationship of the inter-coil strength of the magnetic field to the distance between the coils.

## PART I: Computer Setup

1.	Connect the ScienceWorkshop interface to the computer, turn on the interface, and turn on the computer.

2.	Connect the Rotary Motion Sensor phone plugs to Digital Channel 1 and 2.

3.	Connect the Magnetic Field Sensor DIN plug to Analog Channel A on the interface.

4.	Connect the Power Amplifier to Analog Channel B. Plug the power cord into the back of the Power Amplifier and connect the power cord to an appropriate electrical receptacle.

5.	Open the document titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- | --- |
| P59 Helmholtz Coils.DS | (See end of activity) | (See end of activity) |

•	The DataStudio document opens with a Digits display of magnetic field strength and current and a Graph display of Field Strength vs. Position.

•	See the pages at the end of this activity for information about modifying a ScienceWorkshop file.

•	The Signal Generator is set to output DC at 10.0 V. It is set to Auto so it will start and stop automatically when start and stop measuring data.

## PART II: Sensor Calibration & Equipment Setup

•	You do not need to calibrate the Magnetic Field Sensor or the Power Amplifier. The Magnetic Field Sensor produces a voltage that is directly proportional to the magnetic field strength as follows: 10 millvolts = 10 gauss (where 1000 gauss = 0.1 tesla). The sensor’s range is ±2000 gauss.

•	Note: Depending on the strength of the magnetic field around the coils, you may want to increase the sensitivity of the Magnetic Field Sensor.

Range Select switch: Use this switch to select one of the three input ranges for the sensor. The ranges are as follows:

| Gain | Range | Resolution | Accuracy |
| --- | --- | --- | --- |
| 1X | ±1000 gauss | 0.5 gauss | 100 gauss |
| 10X | ±100 gauss | 0.05 gauss | 10 gauss |
| 100X | ±10 gauss | 0.005 gauss | 1 gauss |

•	For this activity, begin with the Range Select switch on the 1X setting.

### Equipment Setup

1.	Connect the Helmholtz coils in series with the output from the Power Amplifier. Use one patch cord to connect the positive terminal of the Power Amplifier to the positive terminal on the first coil. Use a second patch cord to connect the negative terminal on the first coil to the positive terminal on the second coil. Use the third patch cord to connect the negative terminal on the second coil to the negative terminal on the Power Amplifier.

2.	Measure the radius of a coil. Record the radius in the Data section. Position the two coils so they are one radius, R, apart and parallel to each other.

3.	Construct a ‘track’ for the Magnetic Field Sensor in the following way: Place a laboratory jack on each side of the Helmholtz coils to support the meter stick. Place the meter stick through the Helmholtz coils as shown with the 50-cm mark of the meter stick at the midpoint between the coils.

4.	Adjust the position of the laboratory jacks so they are at least 30 cm from the center of the coils.

5.	Adjust the height of the laboratory jacks so the Magnetic Field Sensor can move along the center line (vertically) of the two coils when it rests on the meter stick. Make sure the meter stick is level.

6.	Remove the ‘O’ ring from the three-step pulley on the Rotary Motion Sensor. Mount the Rotary Motion Sensor on a support rod near the Magnetic Field Sensor.

7.	Attach one end of a string to the Magnetic Field Sensor and place the string on the pulley of the Rotary Motion Sensor. Attach a mass hanger to the other end of the string so the string stays on the pulley of the sensor.

## PART III: Data Recording

1.	Hold the Magnetic Field Sensor away from any magnetic field sources. Zero the sensor by clicking the TARE button on the top of the sensor bos.

2.	Select the AXIAL field by clicking the AXIAL/RADIAL SELECT SWITCH on the top of the Magnetic Field Sensor.

3.	Place the sensor box on top of the meter stick with the end of the sensor rod aligned with the 30-cm mark, facing toward the coils. Hold the sensor in place.

4.	Turn on the power switch on the back of the Power Amplifier.

•	Note: The red light-emitting diode (LED) on the front of the Power Amplifier may light up. This indicates that the Power Amplifier is providing maximum current.

5.	Start measuring data. (Click ‘Start’ in DataStudio or ‘REC’ in ScienceWorkshop.)

6.	Record the value shown in the Digits display for Current in the Data section.

7.	Slowly and steadily move the Magnetic Field Sensor along the meter stick from the 30-cm mark to the 70-cm mark.

• 	Observe the field strength in the Digits display.

8.	Stop measuring data when you reach the 70-cm mark.

9.	Turn off the Power Amplifier.

## Optional

•	Hold the Magnetic Field Sensor in your hand. Click MON to monitor data. Use the sensor to explore the entire volume between the two coils. Pay attention to how much variation there is in the field as the sensor is moved away from the center.

•	If it is possible to change the separation between the coils, repeat the data measurement with the coils separated by 1.5 R instead of R. Change the separation again to 0.5 R and repeat the data measurement.

## Analyzing the Data

1.	Use the Graph display’s built-in analysis tools to find the magnetic field strength midway between the coils.

•	Hint: Use the ‘Smart Tool’ in DataStudio or the ‘Smart Cursor’ () in ScienceWorkshop.

•	Record the magnetic field strength (Y-coordinate) for the midpoint between the coils.

2.	Record the number of turns in one of the coils.

3.	Calculate the theoretical value of the magnetic field at the midpoint between the Helmholtz coils using the measured current, radius, and number of turns for the coil.

4.	Compare the theoretical value to the measured value at the midpoint using a percent difference.

# Record your results in the Lab Report section.

# Lab Report - Activity P59: Magnetic Field of Helmholtz Coils

## What do you think?

The purpose of this activity is to examine the magnetic field produced by the current in a pair of Helmholtz coils, and to measure the magnetic field strength between the coils and compare the measured value to the theoretical value. How does the strength of the magnetic field between the coils relate to the distance of separation between the Helmholtz coils?

## Data

| Item | Value |
| --- | --- |
| Radius of coil |  |
| Number of turn |  |
| Current |  |
| Measured field strength |  |
| Theoretical field strength |  |
| Percent difference |  |

## Questions

1.	Based on your graph, over what distance along the axis can the magnetic field be considered a constant?

2.	How did the measured value of magnetic field strength compare to the theoretical value? What factors may have caused the difference, if any?

## Optional Questions

1.	How uniform is the magnetic field between the coils as the sensor was moved radially outward from the center toward the windings of the coils?

2.	If a different separation of the coils was used, how did that affect the answers to the first two questions?

## Modify an existing ScienceWorkshop file.

### Open the ScienceWorkshop File

Open the file titled as shown:

| ScienceWorkshop (Mac) | ScienceWorkshop (Win) |
| --- | --- |
| P53 Mag. Field Helmholtz | P53_HELM.SWS |

This activity uses the Rotary Motion Sensor to measure the position of the Magnetic Field Sensor as you move the Magnetic Field Sensor through the Helmholtz coils.

•	Add the Rotary Motion Sensor to the Experiment Setup.

•	Modify the Sampling Options.

•	Change the Graph display to include ‘Position’ from the Rotary Motion Sensor.

1.	Click and drag the Digital Sensor Icon plug to Channel 1.

2.	Select ‘Rotary Motion Sensor’ from the list of digital sensors.

3.	In the Experiment Setup window, double-click on the Rotary Motion Sensor icon to open the Sensor Setup window.

4.	Change the Divisions/Rotation from 360 to 1440. Click the Linear Calibration menu and select Large Pulley (Groove) from the menu. Click OK to return to the Experiment Setup window.

5.	Click the Graph to make it active. Click the Horizontal Axis Input Menu button (). Select Digital 1, Position (linPos) from the Input Menu.

•	The Graph will display Strength (gauss) along the vertical axis, and Position (m) along the horizontal axis.

6.	Finally, change the Sampling Options so that the Keyboard Sampling window does not open when you start measuring data.

•	Click the Experiment menu. Select Sampling Options… from the menu to open the Sampling Options window.

•	The Sampling Options window shows that Keyboard is selected, and that the Parameter is Position and the Units are m.

•	Click the check box in front of Keyboard to turn Keyboard Sampling off.

•	Click OK to return to the Experiment Setup window.

7.	Follow the procedure for measuring data as described before. Position the sensor on the meter stick as before. To collect data, click ‘REC’. Begin moving the sensor slowly and steadily through the coils, stopping at the same end position as before. Click ‘STOP’ to stop collecting data.