# Activity SL25: Exponential Modeling – Newton’s Law of Cooling (Temperature Sensor)

| Concept | DataStudio | ScienceWorkshop (Mac) | ScienceWorkshp (Win) |
| --- | --- | --- | --- |
| Exponential modeling | MA11.DS | MA11 | MA11.SWS |

| Equipment Needed | Qty | Consumables | Qty |
| --- | --- | --- | --- |
| Temperature Sensor (CI-6505A) | 1 | Water | 300 mL |
| Beaker, 1000 mL | 1 |  |  |
| Hot plate | 1 |  |  |
| Textbook | 1 |  |  |
| Protective gear | PS |  |  |

## What Do You Think?

From your own experience with the cooling of hot liquids (take coffee or tea for example), name some ways in which you would cause the hot liquid to reach the desired temperature before taking a sip.

Take time to write an answer to this question in the Lab Report section.

## Background

The cooling of a hot beverage is a common daily occurrence. If a hot cup of your favorite brew is allowed to sit for a while, the temperature of the liquid plus the cup ultimately reaches the temperature of its surroundings (room temperature).

The graph of temperature versus time for a hot beverage is a nice example of exponential decay. At first glance, the graph of the cooling process shows a rapid decrease in temperature. A little while later, the graph levels off as it approaches room temperature. Newton observed the rate at which an object cools, ∆T/∆t, depends on how much hotter the object is than its surroundings. This is the reason why the graph shows a greater cooling rate at first, and a leveling off as the object approaches room temperature.

This activity is a simple cooling experiment that lets you model the data using the exponential function ex.

Newton’s Law of Cooling states:

The rate of cooling is directly proportional to the temperature difference between the object and its surroundings, (Tobject - Troom).

Transforming Newton’s Law of Cooling into an equation that relates the temperature of the object as a function of time requires advanced techniques. Leaving the solving to the experts (you could be that expert in future math courses), the equation is:

where T(t) is the temperature at time “t”, T(0) is the initial temperature of the object, Troom is room temperature, and k is a constant of proportionality.

You will determine k using properties of natural logarithms and one of the data points.

| SAFETY REMINDERS Wear protective gear. Follow directions for using the equipment. Be careful when heating the water. |  |  |  |
| --- | --- | --- | --- |

## For You To Do

First, use the Temperature Sensor to measure the room temperature. Then measure the temperature as the sensor cools down to room temperature from an initial temperature of about 100 ˚C. Use DataStudio or ScienceWorkshop to record, display, and analyze the data.

## Pre-Lab

Put 300 mL of water into the 1000-mL beaker and place the beaker on the hot plate. Start heating the water to a boil. Do not leave the hot plate unattended.

## PART I: Computer Setup

1.	Connect the interface to the computer, turn on the interface, and turn on the computer.

2.	Connect the Temperature Sensor to Analog Channel A.

3.	Open the file titled as shown:

| DataStudio | ScienceWorkshop (Mac) | ScienceWorkshp (Win) |
| --- | --- | --- |
| MA11.DS | MA11 | MA11.SWS |

- The DataStudio document has a Workbook display. Read the instructions in the Workbook.

- The ScienceWorkshop document will open with a Digits display, a Table display , and a Graph display of Temperature.

- Data recording is set so there is one measurement per 5 s and Stop Condition = Time at 600 s (10 min.).

## PART II: Sensor Calibration and Equipment Setup

- You do not need to calibrate the Temperature Sensor.

## PART III: Data Recording

- When the water in the beaker is boiling, use the Temperature Sensor and the Digits display to find the room temperature. Start to monitor the temperature of the room.

- Hint: In DataStudio, select “Monitor Data” in the Experiment menu.

- Hint: In ScienceWorkshop, click the MON button.

- Record the room temperature:

Troom = __________

- Put the Temperature Sensor into the boiling water. Watch the Digits display until the temperature reaches a maximum value and remains steady.

- Once the temperature reaches a steady value, QUICKLY do the following:

- Remove the Temperature Sensor from the beaker of boiling water.

- Place the sensor on the textbook with the tip of the sensor extending beyond the edge of the book.

- Click STOP, and then immediately start recording data.

- Hint: In DataStudio, click Start . In ScienceWorkshop, click REC.

- Turn off the hot plate.

- Data recording stops automatically at 600 s (10 minutes).

## Analyzing the Data – Rate of Cooling

- After the recording has stopped, click the Graph display to make it active. Set up your Graph to display statistics.

- Hint: In DataStudio, click the Statistics menu button in the toolbar and select “Show All”.

- Hint: In ScienceWorkshop, click the Statistics button to open the statistics area on the right side of the graph. Click the Statistics menu button and select “All Of The Above”.

- Re-scale the graph to fit the data. Refer to the graph as you answer these questions.

# Write your answers in the Lab Report section.

## Questions

- On your graph, at what point is the rate of cooling the greatest?

- On your graph, over what interval of time is the rate of cooling the greatest?

- On your graph, over what interval of time is the rate of cooling the least?

## Analyzing the Data – Calculation and Curve Fit

- Use data from your Table display and the mathematical model for Newton’s Law of Cooling to calculate “k”, the constant of proportionality.

The mathematical model for Newton’s Law of Cooling is:

where T(t) is the temperature at time “t”, T(0) is the initial temperature of the object, Troom is room temperature, and k is a constant of proportionality.

To determine “k” you will need the initial temperature, the room temperature, and one other temperature selected from your Table.

In this Sample Calculation below, the initial temperature of the Temperature Sensor is 94.53 ˚C. The room temperature is 21.80 ˚C. (Use your own values for these temperatures when you do the calculation.)

To get the other temperature from the Table, click the Time button so the Table shows both time and temperature. Then, select any data pair between t = 20 s and t = 120 s.

For the Sample Calculation below, the sample data pair is (75.0000, 33.35). In other words, at time = 75 seconds, the temperature = 33.35 ˚C.

## Sample Calculation

Initial temperature = 94.53 ˚C

Room temperature = 21.80 ˚C

Data pair from Table: (75, 33.35)

- Use the Curve Fit feature in DataStudio or ScienceWorkshop to apply an Exponential Fit on the graph of your data.

## DataStudio Curve Fit

In the DataStudio Graph display, click the ‘Fit’ menu button and select ‘Natural Exponent’.

Double-click the ‘Natural Exponent Fit’ window to open the Curve Fit window (or click ‘Curve Fit’ in the main toolbar).

Notice the formula for ‘Natural Exponent’:

In the Curve Fit window, click ‘Manual’.

In the ‘Manual’ Curve Fit window, type in your calculation for the proportionality constant, ‘k’, as the value for ‘C (Exponent)’. Then type in the room temperature as ‘B (Y Offset)’. Finally, type in the difference between the initial temperature and the room temperature as ‘A (Scale Factor)’.

Note: The numbers shown are an example. Be sure to enter your numbers.

After you enter your values for the Variables, click ‘Accept’.

Compare the new Curve Fit in the Graph display to your data.

Go to the ‘Curve Fit’ window and adjust your number for ‘C (Exponent)’ slightly. Click ‘Accept’ again to see whether your new numbers improve the Curve Fit on the Graph display.

Try the following: Click ‘Automatic’ in the ‘Curve Fit’ window and then click ‘Accept’. Compare the new Curve Fit to the data in your Graph display.

## ScienceWorkshop Curve Fit

- ScienceWorkshop will attempt to fit the data to a mathematical formula with base “e” raised to a variable in x.

- In ScienceWorkshop you may see a message that says “there is no valid solution.” In other words, the program needs your help to create the mathematical formula that best fits your data. Click ‘OK’ to continue.

- The Exponential Fit is of the form y = a1 + a2e^(a3x + a4), where a1 is the room temperature, a2 = (initial temperature of the hot liquid) – (room temperature), a3 = – k, and finally, a4 has no match according to the function described in the Background. So, let a4 = 0.

ScienceWorkshop Exponential Fit Formula:

- In the Graph statistics area, do the following:

- Click a1 and enter the value of the room temperature.

- Click a2 and enter the difference between the initial (maximum) temperature of the sensor, T(0), and the room temperature.

- Click a3 and enter the constant of proportionality, k, that you calculated earlier.

- Click a4 and enter “0” (zero).

The curve fit may not be exact, but none-the-less, that last entry really made a difference. It is important that parameters a1, a2, and a4, not be changed to better the fit, for they represent the actual initial and final conditions of the experiment. Try inputting different values for k (a3) to see if a better fit is possible.

# Lab Report - Activity SL25: Exponential Modeling – Newton’s Law of Cooling

## What do you think?

From your own experience with the cooling of hot liquids (take coffee or tea for example), name some ways in which you would cause the hot liquid to reach the desired temperature before taking a sip.

## Questions

- On your graph, at what point is the rate of cooling the greatest?

- On your graph, over what interval of time is the rate of cooling the greatest?

- On you graph, over what interval of time is the rate of cooling the least?

- How would the rate of cooling be affected if the Temperature Sensor were allowed to cool in a refrigerator?

- Again, if the Temperature Sensor were allowed to cool in the refrigerator, would k be greater than or smaller than if the Temperature Sensor were allowed to cool at room temperature?

- What would a temperature vs. time graph look like if the Temperature Sensor were allowed to warm up rather than cool down? Is this an example of an exponential function?